openMSP430

Author: Olivier GIRARD
olgirard@gmail.com

Rev. 1.14
December 17, 2013

Revision History
Rev.	Date	Author	Description
1.0	August 4th, 2009	GIRARD	First version.
1.1	August 30th, 2009	GIRARD	Replaced “openMSP430.inc“ with “openMSP430_defines.v“
1.2	December 27th, 2009	GIRARD	- Update file and directory description for hte FPGA projects (in particular, add the Altera project). / - Diverse minor updates.
1.3	December 29th, 2009	GIRARD	- Renamed the “rom_*“ ports to “pmem_*“. / - Renamed the “ram_*“ ports to “dmem_*“. / - Renamed the “ROM_AWIDTH“ Verilog define to “PMEM_AWIDTH“. / - Renamed the “RAM_AWIDTH“ Verilog define to “DMEM_AWIDTH“. / - Prefixed all the verilog sub-modules of the openMSP430 core with “omsp_“. / - Diverse minor updates
1.4	January 12th, 2010	GIRARD	- Added the “Integration and Connectivity“section.
1.5	March 7th, 2010	GIRARD	- Add Hardware multiplier info. / - Added the “Area and Speed Analysis“ section.
1.6	August 1st, 2010	GIRARD	- Update core configuration section. / - Expand the CPU selection table for msp430-gcc.
1.7	August 18th, 2010	GIRARD	- Update CPU_ID description in the serial debug interface chapter..
1.8	March 1st, 2011	GIRARD	- Update openmsp430-minidebug tool section. / - Add. Actel ProASIC3 example to the file and directory description section.
1.9	June 6th, 2011	GIRARD	- General update to reflect the latest RTL implementation (cpu_en/dbg_en ports, configurable peripheral address space, software development tools update...)..
1.10	March 20th, 2012	GIRARD	- Global update reflecting the ASIC support and corresponding configuration options.
1.11	July 15th, 2012	GIRARD	- Add benchmark results / - Add custom memory size configuration
1.12	November 27th, 2012	GIRARD	- Global update reflecting the I2C based serial debug interface update.
1.13	February 24th, 2013	GIRARD	- Minor update to reflect new ASIC_CLOCKING option.
1.14	December 17th, 2013	GIRARD	- Update with number of IRQs configuration option.- / - Move peripherals documentation to a dedicated chapter.

Contents

Overview

Introduction

The openMSP430 is a synthesizable 16bit microcontroller core written in Verilog. It is compatible with Texas Instruments' MSP430 microcontroller family and can execute the code generated by an MSP430 toolchain in a near cycle accurate way.
The core comes with some peripherals (16x16 Hardware Multiplier, Watchdog, GPIO, TimerA, generic templates) and most notably with a two-wire Serial Debug Interface supporting the MSPGCC GNU Debugger (GDB) for in-system software debugging.

While being fully FPGA friendly, this design is also particularly suited for ASIC implementations (typically mixed signal ICs with strong area and low-power requirements).

In a nutshell, the openMSP430 brings with it:

- Low area (8k-Gates), without hidden extra infrastructure overhead (memory backbone, IRQ controller and watchdog timer are already included).
- Excellent code density.
- Good performances.
- Build-in power and clock management options.
- Multiple times Silicon Proven.
Download

Design
The complete tar archive of the project can be downloaded here (OpenCores account required).
The following SVN command can be run from a console (or GUI):
svn export http://opencores.org/ocsvn/openmsp430/openmsp430/trunk/ openmsp430

Changelog

- The Core's ChangeLog lists the CPU updates
- The Tools' ChangeLog lists the Software development tools updates.
- Subscribe to the following RSS feed to keep yourself informed about ALL updates.

Documentation
Being fully compatible with the original MSP430 architecture, TI's official documentation is applicable: SLAU49F.PDF
In addition, the openMSP430 online documentation is also available in pdf.

Features & Limitations
Features
- Core:
  - Full instruction set support.
  - Interrupts: IRQs (x14, x30 or x62), NMI (x1).
  - Low Power Modes (LPMx).
  - Configurable memory size for both program and data.
  - Scalable peripheral address space.
  - Two-wire Serial Debug Interface (I2C or UART based) with GDB support (Nexus class 3, w/o trace).
  - FPGA friendly (option for single clock domain, no clock gate).
  - ASIC friendly (options for full power & clock management support).
  - Small size (Xilinx: 1650 LUTs / Altera: 1550 LEs / ASIC: 8k gates).
- Peripherals:
  - 16x16 Hardware Multiplier.
  - Basic Clock Module.
  - Watchdog.
  - Timer A (FPGA only).
  - GPIO (FPGA only).
  - Templates for 8 and 16 bit peripherals.

Limitations
- Core:
  - Instructions can't be executed from the data memory.

Links
Development has been performed using the following freely available (excellent) tools:
- Icarus Verilog : Verilog simulator.
- GTKWave Analyzer : Waveform viewer.
- MSPGCC : GCC toolchain for the Texas Instruments MSP430 MCUs.
- ISE WebPACK : Xilinx's free FPGA synthesis tool.

A few MSP430 links:
- Wikipedia: MSP430
- TI: MSP430x1xx Family User's Guide
- TI: MSP430 Competitive Benchmarking
- TI: a list of available MSP430 Open Source projects out there on the web today.

Legal information

MSP430 is a trademark of Texas Instruments, Inc. This project is not affiliated in any way with Texas Instruments. All other product names are trademarks or registered trademarks of their respective owners.

Core
Table of content
- 1. Introduction
- 2. Core
  - 2.1 Design structure
  - 2.2 Limitations
  - 2.3 Configuration
    - 2.3.1 Basic System Configuration
    - 2.3.2 Advanced System Configuration
    - 2.3.3 Expert System Configuration
    - 2.3.4 Parameters For Multi-Core Systems
  - 2.4 Memory mapping
  - 2.5 Interrupt mapping
  - 2.6 Pinout
  - 2.7 Instruction Cycles and Lengths
  - 2.8 Serial Debug Interface
  - 2.9 Benchmark results
    - 2.9.1 Dhrystone
    - 2.9.2 CoreMark
1. Introduction

The openMSP430 is a 16-bit microcontroller core compatible with TI's MSP430 family (note that the extended version of the architecture, the MSP430X, isn't supported by this IP). It is based on a Von Neumann architecture, with a single address space for instructions and data.

Depending on the selected configuration, this design can either be:

- FPGA friendly: the core doesn't contain any clock gate and has only a single clock domain. As a consequence, in this mode, the Basic Clock Module peripheral has a few limitations.
- ASIC friendly: the core contains up to all clock management options (clock muxes & low-power modes, fine grained clock gating, …) and is also ready for scan insertion. In this mode, the Basic Clock Module offers all features listed in the official documentation.

It is to be noted that this IP doesn't contain the instruction and data memory blocks internally (these are technology dependent hard macros which are connected to the IP during chip integration). However the core is fully configurable in regard to the supported RAM and/or ROM sizes.

2. Core
2.1 Design structure
The following diagram shows the openMSP430 design structure:

- Frontend: This module performs the instruction Fetch and Decode tasks. It also contains the execution state machine.
- Execution unit: Containing the ALU and the register file, this module executes the current decoded instruction according to the execution state.
- Serial Debug Interface: Contains all the required logic for a Nexus class 3 debugging unit (without trace). Communication with the host is done with a standard two-wire interface following either the UART 8N1 or I2C serial protocol.
- Memory backbone: This block performs a simple arbitration between the frontend and execution-unit for program, data and peripheral memory access.
- Basic Clock Module: Generates MCLK, ACLK, SMCLK and manage the low power modes.
- SFRs: The Special Function Registers block contains diverse configuration registers (NMI, Watchdog, ...).
- Watchdog: Although it is a peripheral, the watchdog is directly included in the core because of its tight links with the NMI interrupts and the PUC reset generation.
- 16x16 Multiplier: The hardware multiplier peripheral is transparently supported by the GCC compiler and is therefore located in the core. It can be included or excluded at will through a Verilog define.
2.2 Limitations
The known core limitations are the following:
Instructions can't be executed from the data memory.
2.3 Configuration
It is possible to configure the openMSP430 core through the openMSP430_defines.v file located in the rtl directory (see file and directory description).
In this section, three sets of adjustable user parameters are discussed in order to customize the core. A fourth set is available for ASIC specific options and will be discussed in the ASIC implementation section.

2.3.1 Basic System Configuration
The basic system can be adjusted with the following set of defines in order to match the target system requirements.

//===================================================================== //===================================================================== //BASIC SYSTEM CONFIGURATION //===================================================================== //===================================================================== // // Note: the sum of program, data and peripheral memory spaces must not // exceed 64 kB // // Program Memory Size: // Uncomment the required memory size //------------------------------------------------------- //`define PMEM_SIZE_CUSTOM //`define PMEM_SIZE_59_KB //`define PMEM_SIZE_55_KB //`define PMEM_SIZE_54_KB //`define PMEM_SIZE_51_KB //`define PMEM_SIZE_48_KB //`define PMEM_SIZE_41_KB //`define PMEM_SIZE_32_KB //`define PMEM_SIZE_24_KB //`define PMEM_SIZE_16_KB //`define PMEM_SIZE_12_KB //`define PMEM_SIZE_8_KB //`define PMEM_SIZE_4_KB `define PMEM_SIZE_2_KB //`define PMEM_SIZE_1_KB // Data Memory Size: // Uncomment the required memory size //------------------------------------------------------- //`define DMEM_SIZE_CUSTOM //`define DMEM_SIZE_32_KB //`define DMEM_SIZE_24_KB //`define DMEM_SIZE_16_KB //`define DMEM_SIZE_10_KB //`define DMEM_SIZE_8_KB //`define DMEM_SIZE_5_KB //`define DMEM_SIZE_4_KB //`define DMEM_SIZE_2p5_KB //`define DMEM_SIZE_2_KB //`define DMEM_SIZE_1_KB //`define DMEM_SIZE_512_B //`define DMEM_SIZE_256_B `define DMEM_SIZE_128_B // Include/Exclude Hardware Multiplier `define MULTIPLIER // Include/Exclude Serial Debug interface `define DBG_EN

The only design considerations at this stage are:
- Make sure that the program and data memories have the correct size :-P
- The sum of program, data and peripheral memory space MUST NOT exceed 64kB.

Note: when selected, full custom memory sizes can be specified in the “Expert System Configuration” section.

2.3.2 Advanced System Configuration
In this section, some additional features are available in order to match the needs of more experienced users.

//============================================================================ //============================================================================ // ADVANCED SYSTEM CONFIGURATION (FOR EXPERIENCED USERS) //============================================================================ //============================================================================ //------------------------------------------------------- // Custom user version number //------------------------------------------------------- // This 5 bit field can be freely used in order to allow // custom identification of the system through the debug // interface. // (see CPU_ID.USER_VERSION field in the documentation) //------------------------------------------------------- `define USER_VERSION 5'b00000 / //------------------------------------------------------- // Include/Exclude Watchdog timer //------------------------------------------------------- // When excluded, the following functionality will be // lost: // - Watchog (both interval and watchdog modes) // - NMI interrupt edge selection // - Possibility to generate a software PUC reset //------------------------------------------------------- `define WATCHDOG //------------------------------------------------------- // Include/Exclude Non-Maskable-Interrupt support //------------------------------------------------------- `define NMI / //------------------------------------------------------- // Number of available IRQs //------------------------------------------------------- // Indicates the number of interrupt vectors supported // (16 ,32 or 64). //------------------------------------------------------- `define IRQ_16 //`define IRQ_32 //`define IRQ_64 / //------------------------------------------------------- // Input synchronizers //------------------------------------------------------- // In some cases, the asynchronous input ports might // already be synchronized externally. // If an extensive CDC design review showed that this // is really the case, the individual synchronizers // can be disabled with the following defines. // // Notes: // - all three signals are all sampled in the MCLK domain // // - the dbg_en signal reset the debug interface // when 0. Therefore make sure it is glitch free. // //------------------------------------------------------- `define SYNC_NMI //`define SYNC_CPU_EN //`define SYNC_DBG_EN / //------------------------------------------------------- // Peripheral Memory Space: //------------------------------------------------------- // The original MSP430 architecture map the peripherals // from 0x0000 to 0x01FF (i.e. 512B of the memory space). // The following defines allow you to expand this space // up to 32 kB (i.e. from 0x0000 to 0x7fff). // As a consequence, the data memory mapping will be // shifted up and a custom linker script will therefore // be required by the GCC compiler. //------------------------------------------------------- //`define PER_SIZE_CUSTOM //`define PER_SIZE_32_KB //`define PER_SIZE_16_KB //`define PER_SIZE_8_KB //`define PER_SIZE_4_KB //`define PER_SIZE_2_KB //`define PER_SIZE_1_KB `define PER_SIZE_512_B / //------------------------------------------------------- // Defines the debugger CPU_CTL.RST_BRK_EN reset value // (CPU break on PUC reset) //------------------------------------------------------- // When defined, the CPU will automatically break after // a PUC occurrence by default. This is typically useful // when the program memory can only be initialized through // the serial debug interface. //------------------------------------------------------- `define DBG_RST_BRK_EN

Design consideration at this stage are:
- Setting a peripheral memory space to something else than 512B will shift the data memory mapping up, which in turn will require the use of a custom linker script. If you don't know what a linker script is and if you don't want to know what it is, you should probably not modify this section.
- The sum of program, data and peripheral memory space MUST NOT exceed 64kB.

Note: when selected, full custom peripheral memory space can be specified in the “Expert System Configuration” section.

2.3.3 Expert System Configuration
In this section, you will find configuration options which will be relevant for roughly 0.1% of the users (according to a highly reliable market analysis ;-) ).

//============================================================================ //============================================================================ // EXPERT SYSTEM CONFIGURATION ( !!!! EXPERTS ONLY !!!! ) //============================================================================ //============================================================================ // // IMPORTANT NOTE: Please update following configuration options ONLY if // you have a good reason to do so... and if you know what // you are doing :-P // //============================================================================ //------------------------------------------------------- // Select serial debug interface protocol //------------------------------------------------------- // DBG_UART -> Enable UART (8N1) debug interface // DBG_I2C -> Enable I2C debug interface //------------------------------------------------------- `define DBG_UART //`define DBG_I2C / //------------------------------------------------------- // Enable the I2C broadcast address //------------------------------------------------------- // For multicore systems, a common I2C broadcast address // can be given to all oMSP cores in order to // synchronously RESET, START, STOP, or STEP all CPUs // at once with a single I2C command. // If you have a single openMSP430 in your system, // this option can stay commented-out. //------------------------------------------------------- //`define DBG_I2C_BROADCAST / //------------------------------------------------------- // Number of hardware breakpoint units (each unit contains // two hardware address breakpoints): // - DBG_HWBRK_0 -> Include hardware breakpoints unit 0 // - DBG_HWBRK_1 -> Include hardware breakpoints unit 1 // - DBG_HWBRK_2 -> Include hardware breakpoints unit 2 // - DBG_HWBRK_3 -> Include hardware breakpoints unit 3 //------------------------------------------------------- // Please keep in mind that hardware breakpoints only // make sense whenever the program memory is not an SRAM // (i.e. Flash/OTP/ROM/...) or when you are interested // in data breakpoints (btw. not supported by GDB). //------------------------------------------------------- //`define DBG_HWBRK_0 //`define DBG_HWBRK_1 //`define DBG_HWBRK_2 //`define DBG_HWBRK_3 / //------------------------------------------------------- // Enable/Disable the hardware breakpoint RANGE mode //------------------------------------------------------- // When enabled this feature allows the hardware breakpoint // units to stop the cpu whenever an instruction or data // access lays within an address range. // Note that this feature is not supported by GDB. //------------------------------------------------------- //`define DBG_HWBRK_RANGE //------------------------------------------------------- // Custom Program/Data and Peripheral Memory Spaces //------------------------------------------------------- // The following values are valid only if the // corresponding *_SIZE_CUSTOM defines are uncommented: // // - *_SIZE : size of the section in bytes. // - *_AWIDTH : address port width, this value must allow // to address all WORDS of the section // (i.e. the *_SIZE divided by 2) //------------------------------------------------------- // Custom Program memory (enabled with PMEM_SIZE_CUSTOM) `define PMEM_CUSTOM_AWIDTH 10 `define PMEM_CUSTOM_SIZE 2048 // Custom Data memory (enabled with DMEM_SIZE_CUSTOM) `define DMEM_CUSTOM_AWIDTH 6 `define DMEM_CUSTOM_SIZE 128 // Custom Peripheral memory (enabled with PER_SIZE_CUSTOM) `define PER_CUSTOM_AWIDTH 8 `define PER_CUSTOM_SIZE 512 //------------------------------------------------------- // ASIC version //------------------------------------------------------- // When uncommented, this define will enable the // ASIC system configuration section (see below) and // will activate scan support for production test. // // WARNING: if you target an FPGA, leave this define // commented. //------------------------------------------------------- //`define ASIC

Design consideration at this stage are:
This is the expert section... so you know what your are doing, right ;-)

All remaining defines located after the ASIC section in the openMSP430_defines.v file are system constants and MUST NOT be edited.

2.3.4 Parameters For Multi-Core Systems
In addition to the define file, two Verilog parmaeters are available to facilitate software development on multi-core systems.
For example, in a dual-core openMSP430 system, the cores can be instantiated as following:

openMSP430 #(.INST_NR (0), .TOTAL_NR(1)) openMSP430_core_0 ( ... ); openMSP430 #(.INST_NR (1), .TOTAL_NR(1)) openMSP430_core_1 ( ... );

The values of these parameters are then directly accessible through the CPU_NR register of the SFR peripheral.
For example, if both cores share the same program memory, the software can take advantage of this information as following:

"... int main(void) { if (CPU_NR==0x0100) { main_core_0(); // Main routine call for core 0 } if (CPU_NR==0x0101) { main_core_1(); // Main routine call for core 1 } } …"

2.4 Memory mapping

As discussed earlier, the openMSP430 memory mapping is fully configurable.
The basic system configuration section allows to adjust program and data memory sizes while keeping 100% compatibility with the pre-existing linker scripts provided by MSPGCC (or any other toolchain for that matter).
However, an increasing number of users saw the 512B space available for peripherals in the standard MSP430 architecture as a limitation. Therefore, the advanced system configuration section gives the possibility to up-scale the reserved peripheral address space anywhere between 512B and 32kB. As a consequence, the data memory space will be shifted up, which means that the linker script of your favorite toolchain will have to be modified accordingly.

The following schematic should hopefully summarize this:
2.5 Interrupt mapping

The number of supported interrupts is configurable with the IRQ_xx macros.
The interrupt vectors are then mapped as following:

2.6 Pinout

The full pinout of the openMSP430 core is provided in the following table:

Port Name	Direction	Width	Clock / Domain	Description
Clocks
cpu_en	Input	1	<async> / or mclk4	Enable CPU code execution (asynchronous and non-glitchy). / Set to 1 if unused.
dco_clk	Input	1	-	Fast oscillator (fast clock)
lfxt_clk	Input	1	-	Low frequency oscillator (typ. 32kHz) / Set to 0 if unused.
mclk	Output	1	-	Main system clock
aclk_en	Output	1	mclk	FPGA ONLY: ACLK enable
smclk_en	Output	1	mclk	FPGA ONLY: SMCLK enable
dco_enable	Output	1	dco_clk	ASIC ONLY: Fast oscillator enable
dco_wkup	Output	1	<async>	ASIC ONLY: Fast oscillator wakeup (asynchronous)
lfxt_enable	Output	1	lfxt_clk	ASIC ONLY: Low frequency oscillator enable
lfxt_wkup	Output	1	<async>	ASIC ONLY: Low frequency oscillator wakeup (asynchronous)
aclk	Output	1	-	ASIC ONLY: ACLK
smclk	Output	1	-	ASIC ONLY: SMCLK
wkup	Input	1	<async>	ASIC ONLY: System Wake-up (asynchronous and non-glitchy) / Set 0 if unused.
Resets
puc_rst	Output	1	mclk	Main system reset
reset_n	Input	1	<async>	Reset Pin (active low, asynchronous and non-glitchy)
Interrupts
irq	Input	`IRQ_NR-2 1	mclk	Maskable interrupts (one-hot signal)
nmi	Input	1	<async> / or mclk4	Non-maskable interrupt (asynchronous and non-glitchy) / Set to 0 if unused.
irq_acc	Output	IRQ_NR-2 1	mclk	Interrupt request accepted (one-hot signal)
Program Memory interface
pmem_addr	Output	`PMEM_ / AWIDTH1	mclk	Program Memory address
pmem_cen	Output	1	mclk	Program Memory chip enable (low active)
pmem_din	Output	16	mclk	Program Memory data input (optional2)
pmem_dout	Input	16	mclk	Program Memory data output
pmem_wen	Output	2	mclk	Program Memory write byte enable (low active) (optional2)
Data Memory interface
dmem_addr	Output	`DMEM_ / AWIDTH1	mclk	Data Memory address
dmem_cen	Output	1	mclk	Data Memory chip enable (low active)
dmem_din	Output	16	mclk	Data Memory data input
dmem_dout	Input	16	mclk	Data Memory data output
dmem_wen	Output	2	mclk	Data Memory write byte enable (low active)
External Peripherals interface
per_addr	Output	14	mclk	Peripheral address
per_din	Output	16	mclk	Peripheral data input
per_dout	Input	16	mclk	Peripheral data output
per_en	Output	1	mclk	Peripheral enable (high active)
per_we	Output	2	mclk	Peripheral write enable (high active)
Serial Debug interface
dbg_en	Input	1	<async> / or mclk4	Debug interface enable (asynchronous) 3
dbg_freeze	Output	1	mclk	Freeze peripherals
dbg_uart_txd	Output	1	mclk	Debug interface: UART TXD
dbg_uart_rxd	Input	1	<async>	Debug interface: UART RXD (asynchronous)
dbg_i2c_addr	Input	7	mclk	Debug interface: I2C Address
dbg_i2c_broadcast	Input	7	mclk	Debug interface: I2C Broadcast Address (for multicore systems)
dbg_i2c_scl	Input	1	<async>	Debug interface: I2C SCL (asynchronous)
dbg_i2c_sda_in	Input	1	<async>	Debug interface: I2C SDA IN (asynchronous)
dbg_i2c_sda_out	Output	1	mclk	Debug interface: I2C SDA OUT
Scan
scan_enable	Input	1	dco_clk	ASIC ONLY: Scan enable (active during scan shifting)
scan_mode	Input	1	<stable>	ASIC ONLY: Scan mode

1: This parameter is declared in the "openMSP430_defines.v" file and defines the RAM/ROM size or the number of interrupts vectors (16, 32 or 64).
2: These two optional ports can be connected whenever the program memory is a RAM. This will allow the user to load a program through the serial debug interface and to use software breakpoints.
3: When disabled, the debug interface is hold into reset (and clock gated in ASIC mode). As a consequence, the dbg_en port can be used to reset the debug interface without disrupting the CPU execution.
4: Clock domain is selectable through configuration in the “openMSP430_defines.v” file (see Advanced System Configuration).

Note: in the FPGA configuration, the ASIC ONLY signals must be left unconnected (for the outputs) and tied low (for the inputs).

2.7 Instruction Cycles and Lengths

Please note that a detailed description of the instruction and addressing modes can be found in the MSP430x1xx Family User's Guide (Chapter 3).
The number of CPU clock cycles required for an instruction depends on the instruction format and the addressing modes used, not the instruction itself.
In the following tables, the number of cycles refers to the main clock (MCLK). Differences with the original MSP430 are highlighted in green (the original value being red).
Interrupt and Reset Cycles
Action	No. of Cycles	Length of Instruction
Return from interrupt (RETI)	5	1
Interrupt accepted	6	-
WDT reset	4	-
Reset (!RST/NMI)	4	-

- Format-II (Single Operand) Instruction Cycles and Lengths
Addressing Mode	No. of Cycles			Length of Instruction
	RRA, RRC, SWPB, SXT	PUSH	CALL
Rn	1	3	3 (4)	1
@Rn	3	4	4	1
@Rn+	3	4 (5)	4 (5)	1
#N	N/A	4	5	2
X(Rn)	4	5	5	2
EDE	4	5	5	2
&EDE	4	5	5	2

Format-III (Jump) Instruction Cycles and Lengths
All jump instructions require one code word, and take two CPU cycles to execute, regardless of whether the jump is taken or not.

Format-I (Double Operand) Instruction Cycles and Lengths
Addressing Mode		No. of Cycles	Length of Instruction
Src	Dst
Rn	Rm	1	1
	PC	2	1
	x(Rm)	4	2
	EDE	4	2
	&EDE	4	2
@Rn	Rm	2	1
	PC	3 (2)	1
	x(Rm)	5	2
	EDE	5	2
	&EDE	5	2
@Rn+	Rm	2	1
	PC	3	1
	x(Rm)	5	2
	EDE	5	2
	&EDE	5	2
#N	Rm	2	2
	PC	3	2
	x(Rm)	5	3
	EDE	5	3
	&EDE	5	3
x(Rn)	Rm	3	2
	PC	3 (4)	2
	x(Rm)	6	3
	EDE	6	3
	&EDE	6	3
EDE	Rm	3	2
	PC	3 (4)	2
	x(Rm)	6	3
	EDE	6	3
	&EDE	6	3
&EDE	Rm	3	2
	PC	3	2
	x(Rm)	6	3
	EDE	6	3
	&EDE	6	3

2.8 Serial Debug Interface

All the details about the Serial Debug Interface are located here.

2.9 Benchmark results
2.9.1 Dhrystone (DMIPS/MHz)
Dhrystone is known for being susceptible to compiler optimizations (among other issues).
However, as it is still quite a popular metric, some results are provided here (ranging from 0.30 to 0.45 DMIPS/MHz depending on the compiler version and options).
Note that the used C-code is available in the repository here and here.

Dhrystone flavor	Compiler options	-Os	-O2	-O3
	Compiler version
Dhrystone v2.1 (common version)	mspgcc v4.4.5	0.30	0.32	0.33
	mspgcc v4.6.3	0.37	0.39	0.40
Dhrystone v2.1 (MCU adapted)	mspgcc v4.4.5	0.30	0.30	0.31
	mspgcc v4.6.3	0.37	0.44	0.45

2.9.2 CoreMark (Coremark/MHz)
CoreMark tries to address most of Dhrystone's pitfall by preventing the compiler to optimize some code away and using "real-life" algorithm.
Note that the used C-code is available in the repository here.

	Compiler options	-Os	-O2	-O3
	Compiler version
CoreMark v1.0 / (official version)	mspgcc v4.4.5	0.78	0.85	0.83
	mspgcc v4.6.3	0.74	0.91	0.87

Peripherals
Table of content
- 1. Introduction
- 2. Peripherals
  - 2.1 System Peripherals
    - 2.1.1 Basic Clock Module: FPGA
    - 2.1.2 Basic Clock Module: ASIC
    - 2.1.3 SFR
    - 2.1.4 Watchdog Timer
    - 2.1.5 16x16 Hardware Multiplier
  - 2.2 External Peripherals
    - 2.2.1 Digital I/O (FPGA ONLY)
    - 2.3.2 Timer A (FPGA ONLY)
1. Introduction
In addition to the CPU core itself, several peripherals are also provided and can be easily connected to the core during integration.

2. Peripherals
2.1 System Peripherals
In addition to the CPU core itself, several peripherals are also provided and can be easily connected to the core during integration. The followings are directly integrated within the core because of their tight links with the CPU.
It is to be noted that ALL system peripherals support both ASIC and FPGA versions.

2.1.1 Basic Clock Module: FPGA
In order to make an FPGA implementation as simple as possible (ideally, a non-professional designer should be able to do it), clock gates are not used in the design configuration and neither are clock muxes.

With these constrains, the Basic Clock Module is implemented as following:

Note: CPUOFF doesn't switch MCLK off and will instead bring the CPU state machines in an IDLE state while MCLK will still be running.

In order to 'clock' a register with ACLK or SMCLK, the following structure needs to be implemented:

For example, the following Verilog code would implement a counter clocked with SMCLK:

reg [7:0] test_cnt; / always @ (posedge mclk or posedge puc_rst) / if (puc_rst) test_cnt <= 8'h00; / else if (smclk_en) test_cnt <= test_cnt + 8'h01;

Register Description
- DCOCTL: Not implemented
- BCSCTL1:
  - BCSCTL1[7:6]: Unused
  - BCSCTL1[5:4]: DIVAx
  - BCSCTL1[4:0]: Unused
- BCSCTL2:
  - BCSCTL2[7:4]: Unused
  - BCSCTL2[3] : SELS
  - BCSCTL2[2:1]: DIVSx
  - BCSCTL2[0] : Unused

2.1.2 Basic Clock Module: ASIC

When targeting an ASIC, up to all clock management options available in the MSP430x1xx Family User's Guide (Chapter 4) can be included:

Additional info can be found in the ASIC implementation section.

2.1.3 SFR
Following the MSP430x1xx Family User's Guide, this peripheral implements flags and interrupt enable bits for the Watchdog Timer and NMI:

Register Name	Address	Bit Fields
		7	6	5	4	3	2	1	0
IE1	0x0000	Reserved			NMIIE 1	Reserved			WDTIE 2
IFG1	0x0002	Reserved			NMIIFG 1	Reserved			WDTIFG 2

1: These fields are not available if the NMI is excluded (see openMSP430_defines.v )
2: These fields are not available if the Watchdog is excluded (see openMSP430_defines.v )

In addition, two 16-bit read-only registers have been added in order to let the software know with which version of the openMSP430 it is running:

Register Name	Address	Bit field
		15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
CPU_ID_LO	0x0004	PER_SPACE					USER_VERSION					ASIC	CPU_VERSION
CPU_ID_HI	0x0006	PMEM_SIZE					DMEM_SIZE					MPY
CPU_NR	0x0008	CPU_TOTAL_NR					CPU_INST_NR

- CPU_VERSION	: Current CPU version.
- ASIC	: Defines if the ASIC specific features are enabled in the
  current openMSP430 implementation.
- USER_VERSION	: Reflects the value defined in the openMSP430_defines.v
  file.
- PER_SPACE	: Peripheral address space for the current implementation
  (byte size = PER_SPACE*512)
- MPY	: This bit is set if the hardware multiplier is inclued in the
  current implementation.
- DMEM_SIZE	: Data memory size for the current implementation
  (byte size = DMEM_SIZE*128)
- PMEM_SIZE	: Program memory size for the current implementation
  (byte size = PMEM_SIZE*1024)
- CPU_INST_NR	: Current oMSP instance number (for multicore systems)
- CPU_TOTAL_NR	: Total number of oMSP instances-1 (for multicore systems)

Note: attentive readers will have noted that CPU_ID_LO, CPU_ID_HI and CPU_NR are identical to the Serial Debug Interface register counterparts.

2.1.4 Watchdog Timer

100% of the features advertised in the MSP430x1xx Family User's Guide (Chapter 10) have been implemented.

The following parameter in the openMSP430_defines.v file controls if the watchdog timer should be included or not:

//------------------------------------------------------- / // Include/Exclude Watchdog timer / //------------------------------------------------------- / // When excluded, the following functionality will be / // lost: / // - Watchdog (both interval and watchdog modes) / // - NMI interrupt edge selection / // - Possibility to generate a software PUC reset / //------------------------------------------------------- / `define WATCHDOG

2.1.5 16x16 Hardware Multiplier

100% of the features advertised in the MSP430x1xx Family User's Guide (Chapter 7) have been implemented.

The following parameter in the openMSP430_defines.v file controls if the hardware multiplier should be included or not:

// Include/Exclude Hardware Multiplier / `define MULTIPLIER

2.2 External Peripherals

The external peripherals labeled with the “FPGA ONLY” tag do not contain any clock gate nor clock muxes and are clocked with MCLK only. This mean that they don't support any of the low power modes and therefore are most likely not suited for an ASIC implementation.

2.2.1 Digital I/O (FPGA ONLY)
100% of the features advertised in the MSP430x1xx Family User's Guide (Chapter 9) have been implemented.
The following Verilog parameters will enable or disable the corresponding ports in order to save area (i.e. FPGA utilization):

parameter P1_EN = 1'b1; // Enable Port 1 / parameter P2_EN = 1'b1; // Enable Port 2 / parameter P3_EN = 1'b0; // Enable Port 3 / parameter P4_EN = 1'b0; // Enable Port 4 / parameter P5_EN = 1'b0; // Enable Port 5 / parameter P6_EN = 1'b0; // Enable Port 6

They can be updated as following during the module instantiation (here port 1, 2 and 3 are enabled):
gpio #( .P1_EN(1), / .P2_EN(1), / .P3_EN(1), / .P4_EN(0), / .P5_EN(0), / .P6_EN(0)) gpio_0 (

The full pinout of the GPIO module is provided in the following table:
Port Name	Direction	Width	Description
Clocks & Resets
mclk	Input	1	Main system clock
puc_rst	Input	1	Main system reset
Interrupts
irq_port1	Output	1	Port 1 interrupt
irq_port2	Output	1	Port 2 interrupt
External Peripherals interface
per_addr	Input	8	Peripheral address
per_din	Input	16	Peripheral data input
per_dout	Output	16	Peripheral data output
per_en	Input	1	Peripheral enable (high active)
per_wen	Input	2	Peripheral write enable (high active)
Port 1
p1_din	Input	8	Port 1 data input
p1_dout	Output	8	Port 1 data output
p1_dout_en	Output	8	Port 1 data output enable
p1_sel	Output	8	Port 1 function select
Port 2
p2_din	Input	8	Port 2 data input
p2_dout	Output	8	Port 2 data output
p2_dout_en	Output	8	Port 2 data output enable
p2_sel	Output	8	Port 2 function select
Port 3
p3_din	Input	8	Port 3 data input
p3_dout	Output	8	Port 3 data output
p3_dout_en	Output	8	Port 3 data output enable
p3_sel	Output	8	Port 3 function select
Port 4
p4_din	Input	8	Port 4 data input
p4_dout	Output	8	Port 4 data output
p4_dout_en	Output	8	Port 4 data output enable
p4_sel	Output	8	Port 4 function select
Port 5
p5_din	Input	8	Port 5 data input
p5_dout	Output	8	Port 5 data output
p5_dout_en	Output	8	Port 5 data output enable
p5_sel	Output	8	Port 5 function select
Port 6
p6_din	Input	8	Port 6 data input
p6_dout	Output	8	Port 6 data output
p6_dout_en	Output	8	Port 6 data output enable
p6_sel	Output	8	Port 6 function select

2.2.2 Timer A (FPGA ONLY)
100% of the features advertised in the MSP430x1xx Family User's Guide (Chapter 11) have been implemented.
The full pinout of the Timer A module is provided in the following table:
Port Name	Direction	Width	Description
Clocks, Resets & Debug
mclk	Input	1	Main system clock
aclk_en	Input	1	ACLK enable (from CPU)
smclk_en	Input	1	SMCLK enable (from CPU)
inclk	Input	1	INCLK external timer clock (SLOW)
taclk	Input	1	TACLK external timer clock (SLOW)
puc_rst	Input	1	Main system reset
dbg_freeze	Input	1	Freeze Timer A counter
Interrupts
irq_ta0	Output	1	Timer A interrupt: TACCR0
irq_ta1	Output	1	Timer A interrupt: TAIV, TACCR1, TACCR2
irq_ta0_acc	Input	1	Interrupt request TACCR0 accepted
External Peripherals interface
per_addr	Input	8	Peripheral address
per_din	Input	16	Peripheral data input
per_dout	Output	16	Peripheral data output
per_en	Input	1	Peripheral enable (high active)
per_wen	Input	2	Peripheral write enable (high active)
Capture/Compare Unit 0
ta_cci0a	Input	1	Timer A capture 0 input A
ta_cci0b	Input	1	Timer A capture 0 input B
ta_out0	Output	1	Timer A output 0
ta_out0_en	Output	1	Timer A output 0 enable
Capture/Compare Unit 1
ta_cci1a	Input	1	Timer A capture 1 input A
ta_cci1b	Input	1	Timer A capture 1 input B
ta_out1	Output	1	Timer A output 1
ta_out1_en	Output	1	Timer A output 1 enable
Capture/Compare Unit 2
ta_cci2a	Input	1	Timer A capture 2 input A
ta_cci2b	Input	1	Timer A capture 2 input B
ta_out2	Output	1	Timer A output 2
ta_out2_en	Output	1	Timer A output 2 enable

Note: for the same reason as with the Basic Clock Module FPGA version, the two additional clock inputs (TACLK and INCLK) are internally synchronized with the MCLK domain. As a consequence, TACLK and INCLK should be at least 2 times slowlier than MCLK, and if these clock are used toghether with the Timer A output unit, some jitter might be observed on the generated output. If this jitter is critical for the application, ACLK and INCLK should idealy be derivated from DCO_CLK.

Serial Debug Interface
Table of content
- 1. Introduction
- 2. Debug Unit
  - 2.1 Register Mapping
  - 2.2 CPU Control/Status Registers
    - 2.2.1 CPU_ID
    - 2.2.2 CPU_CTL
    - 2.2.3 CPU_STAT
    - 2.2.4 CPU_NR
  - 2.3 Memory Access Registers
    - 2.3.1 MEM_CTL
    - 2.3.2 MEM_ADDR
    - 2.3.3 MEM_DATA
    - 2.3.4 MEM_CNT
  - 2.4 Hardware Breakpoint Unit Registers
    - 2.4.1 BRKx_CTL
    - 2.4.2 BRKx_STAT
    - 2.4.3 BRKx_ADDR0
    - 2.4.4 BRKx_ADDR1
- 3 Debug Communication Interface: UART
  - 3.1 Serial communication protocol: 8N1
  - 3.2 Synchronization frame
  - 3.3 Read/Write access to the debug registers
    - 3.3.1 Command Frame
    - 3.3.2 Write access
    - 3.3.3 Read access
  - 3.4 Read/Write burst implementation for the CPU Memory access
    - 3.4.1 Write Burst access
    - 3.4.2 Read Burst access
- 4 Debug Communication Interface: I2C
  - 4.1 I2C communication protocol
  - 4.2 Synchronization frame
  - 4.3 Read/Write access to the debug registers
    - 4.3.1 Command Frame
    - 4.3.2 Write access
    - 4.3.3 Read access
  - 4.4 Read/Write burst implementation for the CPU Memory access
    - 4.4.1 Write Burst access
    - 4.4.2 Read Burst access

1. Introduction

The original MSP430 from TI provides a serial debug interface to allow in-system software debugging. In that case, the communication with the host computer is typically built on a JTAG or Spy-Bi-Wire serial protocol. However, the global debug architecture from the MSP430 is unfortunately poorly documented on the web (and is also probably tightly linked with the internal core architecture).
A custom module has therefore been implemented for the openMSP430. The communication with the host is done with a simple two-wire cable following either the UART or I2C serial protocol (interface is selectable in the Expert System Configuration section).
The debug unit provides all required features for Nexus Class 3 debugging (beside trace), namely:

Debug unit features
CPU control (run, stop, step, reset). / Software & hardware breakpoint support. / Hardware watchpoint support. / Memory read/write on-the-fly (no need to halt execution). / CPU registers read/write on-the-fly (no need to halt execution).

Depending on the selected serial interface, the following features are available:

Debug unit features
UART	I2C
Strengths: / No extra hardware required for most FPGA boards (almost all come with a UART interface, either RS232 or USB based. / Possibility to use USB to serial TTL cables. / Weaknesses: / Need to reset the debug interface after cable insertion. / For ASICs, no possibility to change the MCLK frequency during a debug session.	Strengths: / Very stable interface (synchronous protocol, no synchronization frame required). / Multi-core chip support with a single I2C interface (i.e. TWO pins)... in such a system, each openMSP430 instance has its own I2C device address. / Possibility to combine the openMSP430 debug interface with an already existing “functional” I2C interface... effectively creating a ZERO wire serial debug interface. / Affordable USB-ISS adapter (≈23€). / Weaknesses: / Extra I2C adapter required (USB-ISS currently supported).

2. Debug Unit
2.1 Register Mapping
The following table summarize the complete debug register set accessible through the debug communication interface:
Register Name	Address	Bit Field
		15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
CPU_ID_LO	0x00	PER_SPACE					USER_VERSION					ASIC	CPU_VERSION
CPU_ID_HI	0x01	PMEM_SIZE					DMEM_SIZE					MPY
CPU_CTL	0x02	Reserved					CPU_RST	RST_BRK_EN	FRZ_BRK_EN	SW_BRK_EN	ISTEP	RUN	HALT
CPU_STAT	0x03	Reserved					HWBRK3_PND	HWBRK2_PND	HWBRK1_PND	HWBRK0_PND	SWBRK_PND	PUC_PND	Res.	HALT_RUN
MEM_CTL	0x04	Reserved					B/W	MEM/REG	RD/WR	START
MEM_ADDR	0x05	MEM_ADDR[15:0]
MEM_DATA	0x06	MEM_DATA[15:0]
MEM_CNT	0x07	MEM_CNT[15:0]
BRK0_CTL	0x08	Reserved					RANGE_MODE	INST_EN	BREAK_EN	ACCESS_MODE
BRK0_STAT	0x09	Reserved					RANGE_WR	RANGE_RD	ADDR1_WR	ADDR1_RD	ADDR0_WR	ADDR0_RD
BRK0_ADDR0	0x0A	BRK_ADDR0[15:0]
BRK0_ADDR1	0x0B	BRK_ADDR1[15:0]
BRK1_CTL	0x0C	Reserved					RANGE_MODE	INST_EN	BREAK_EN	ACCESS_MODE
BRK1_STAT	0x0D	Reserved					RANGE_WR	RANGE_RD	ADDR1_WR	ADDR1_RD	ADDR0_WR	ADDR0_RD
BRK1_ADDR0	0x0E	BRK_ADDR0[15:0]
BRK1_ADDR1	0x0F	BRK_ADDR1[15:0]
BRK2_CTL	0x10	Reserved					RANGE_MODE	INST_EN	BREAK_EN	ACCESS_MODE
BRK2_STAT	0x11	Reserved					RANGE_WR	RANGE_RD	ADDR1_WR	ADDR1_RD	ADDR0_WR	ADDR0_RD
BRK2_ADDR0	0x12	BRK_ADDR0[15:0]
BRK2_ADDR1	0x13	BRK_ADDR1[15:0]
BRK3_CTL	0x14	Reserved					RANGE_MODE	INST_EN	BREAK_EN	ACCESS_MODE
BRK3_STAT	0x15	Reserved					RANGE_WR	RANGE_RD	ADDR1_WR	ADDR1_RD	ADDR0_WR	ADDR0_RD
BRK3_ADDR0	0x16	BRK_ADDR0[15:0]
BRK3_ADDR1	0x17	BRK_ADDR1[15:0]
CPU_NR	0x18	CPU_TOTAL_NR					CPU_INST_NR

2.2 CPU Control/Status Registers
2.2.1 CPU_ID
This 32 bit read-only register holds the program and data memory size information of the implemented openMSP430.
Register Name	Address	Bit Field
		15	14	13	12	11	10	9	8	7	6	5	4	3	2	1		0
CPU_ID_LO	0x00	PER_SPACE					USER_VERSION					ASIC	CPU_VERSION
CPU_ID_HI	0x01	PMEM_SIZE					DMEM_SIZE					MPY

• CPU_VERSION	: Current CPU version
• ASIC	: Defines if the ASIC specific features are enabled in the current openMSP430 implementation.
• USER_VERSION	: Reflects the value defined in the openMSP430_defines.v file
• PER_SPACE	: Peripheral address space for the current implementation (byte size = PER_SPACE*512)
• MPY	: This bit is set if the hardware multiplier is included in the current implementation.
• DMEM_SIZE	: Data memory size for the current implementation (byte size = DMEM_SIZE * 128)
• PMEM_SIZE	: Program memory size for the current implementation (byte size = PMEM_SIZE * 1024)

2.2.2 CPU_CTL
This 8 bit read-write register is used to control the CPU and to configure some basic debug features. After a POR, this register is set to 0x10 or 0x30 (depending on the DBG_RST_BRK_EN configuration option).
Register Name	Address	Bit Field
		7	6	5	4	3	2	1	0
CPU_CTL	0x02	Res.	CPU_RST	RST_BRK_EN	FRZ_BRK_EN	SW_BRK_EN	ISTEP	RUN	HALT

• CPU_RST	: Setting this bit to 1 will activate the PUC reset. Setting it back to 0 will release it.
• RST_BRK_EN	: If set to 1, the CPU will automatically break after a PUC occurrence.
• FRZ_BRK_EN	: If set to 1, the timers and watchdog are frozen when the CPU is halted.
• SW_BRK_EN	: Enables the software breakpoint detection.
• ISTEP1	: Writing 1 to this bit will perform a single instruction step if the CPU is halted.
• RUN1	: Writing 1 to this bit will get the CPU out of halt state.
• HALT1	: Writing 1 to this bit will put the CPU in halt state.

1:this field is write-only and always reads back 0.

2.2.3 CPU_STAT
This 8 bit read-write register gives the global status of the debug interface. After a POR, this register is set to 0x00.
Register Name	Address	Bit Field
		7	6	5	4	3	2	1	0
CPU_STAT	0x03	HWBRK3_PND	HWBRK2_PND	HWBRK1_PND	HWBRK0_PND	SWBRK_PND	PUC_PND	Res.	HALT_RUN

• HWBRK3_PND	: This bit reflects if one of the Hardware Breakpoint Unit 3 status bit is set (i.e. BRK3_STAT≠0).
• HWBRK2_PND	: This bit reflects if one of the Hardware Breakpoint Unit 2 status bit is set (i.e. BRK2_STAT≠0).
• HWBRK1_PND	: This bit reflects if one of the Hardware Breakpoint Unit 1 status bit is set (i.e. BRK1_STAT≠0).
• HWBRK0_PND	: This bit reflects if one of the Hardware Breakpoint Unit 0 status bit is set (i.e. BRK0_STAT≠0).
• SWBRK_PND	: This bit is set to 1 when a software breakpoint occurred. It can be cleared by writing 1 to it.
• PUC_PND	: This bit is set to 1 when a PUC reset occurred. It can be cleared by writing 1 to it.
• HALT_RUN	: This read-only bit gives the current status of the CPU:
	0 - CPU is running. / 1 - CPU is stopped.

2.2.4 CPU_NR
This 16 bit read only register gives useful information for multi-core systems.
Register Name	Address	Bit Field
		15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
CPU_NR	0x18	CPU_TOTAL_NR					CPU_INST_NR

• CPU_TOTAL_NR	: Total number of oMSP instances – 1 (for multicore systems).
• CPU_INST_NR	: Current oMSP instance number (for multicore systems).

2.3 Memory Access Registers
The following four registers enable single and burst read/write access to both CPU-Registers and full memory address range.

In order to perform an access, the following sequences are typically done:
- single read access (MEM_CNT=0):
  - set MEM_ADDR with the memory address (or register number) to be read
  - set MEM_CTL (in particular RD/WR=0 and START=1)
  - read MEM_DATA
- single write access (MEM_CNT=0):
  - set MEM_ADDR with the memory address (or register number) to be written
  - set MEM_DATA with the data to be written
  - set MEM_CTL (in particular RD/WR=1 and START=1)
- burst read/write access (MEM_CNT≠0):
     ◦ burst access are optimized for the communication interface used (i.e. for the UART). The burst sequence are therefore described in the corresponding section (3.4 Read/Write burst implementation for the CPU Memory access)
2.3.1 MEM_CTL
This 8 bit read-write register is used to control the Memory and CPU-Register read/write access. After a POR, this register is set to 0x00.
Register Name	Address	Bit Field
		7	6	5	4	3	2	1	0
MEM_CTL	0x04	Reserved				B/W	MEM/REG	RD/WR	START

• B/W :	0 - 16 bit access.
	1 - 8 bit access (not valid for CPU-Registers).
• MEM/REG :	0 - Memory access.
	1 - CPU-Register access.
• RD/WR :	0 - Read access.
	1 - Write access.
• START :	0- Do nothing
	1 - Initiate memory transfer.

2.3.2 MEM_ADDR
This 16 bit read-write register specifies the Memory or CPU-Register address to be used for the next read/write transfer. After a POR, this register is set to 0x0000.
Note: in case of burst (i.e. MEM_CNT≠0), this register specifies the first address of the burst transfer and will be incremented automatically as the burst goes (by 1 for 8-bit access and by 2 for 16-bit access).
Register Name	Address	Bit Field
		15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
MEM_ADDR	0x05	MEM_ADDR[15:0]

• MEM_ADDR	: Memory or CPU-Register address to be used for the next read/write transfer.

2.3.3 MEM_DATA
This 16 bit read-write register gives (wr) or receive (rd) the Memory or CPU-Register data for the next transfer. After a POR, this register is set to 0x0000.
Register Name	Address	Bit Field
		15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
MEM_DATA	0x06	MEM_DATA[15:0]

• MEM_DATA	: if MEM_CTL.WR - data to be written during the next write transfer.
	if MEM_CTL.RD - updated with the data from the read transfer

2.3.4 MEM_CNT
This 16 bit read-write register controls the burst access to the Memory or CPU-Registers. If set to 0, a single access will occur, otherwise, a burst will be performed. The burst being optimized for the communication interface, more details are given there. After a POR, this register is set to 0x0000.
Register Name	Address	Bit Field
		15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
MEM_CNT	0x07	MEM_CNT[15:0]

• MEM_CNT	: =0 - a single access will be performed with the next transfer.
	≠0 - specifies the burst size for the next transfer (i.e number of data access). This field will be automatically decremented as the burst goes.

2.4 Hardware Breakpoint Unit Registers
Depending on the defines located in the "openMSP430_defines.v" file, up to four hardware breakpoint units can be included in the design. These units can be individually controlled with the following registers.

2.4.1 BRKx_CTL
This 8 bit read-write register controls the hardware breakpoint unit x. After a POR, this register is set to 0x00.
Register Name	Address	Bit Field
		7	6	5	4	3	2	1	0
BRKx_CTL	0x08, 0x0C, 0x10, 0x14	Reserved			RANGE_MODE	INST_EN	BREAK_EN	ACCESS_MODE

• RANGE_MODE	: 0 - Address match on BRK_ADDR0 or BRK_ADDR1 (normal mode)
	1 - Address match on BRK_ADDR0→BRK_ADDR1 range / (range mode) / Note: range mode is not supported by the core unless the `DBG_HWBRK_RANGE define is set to 1'b1 in the openMSP430_define.v file.
• INST_EN	: 0 - Checks are done on the execution unit (data flow).
	1 - Checks are done on the frontend (instruction flow).
• BREAK_EN	: 0 - Watchpoint mode enable (don't stop on address match).
	1 - Breakpoint mode enable (stop on address match).
• ACCESS_MODE	: 00 - Disabled
	01 - Detect read access. / 10 - Detect write access. / 11 - Detect read/write access / Note: '10' & '11' modes are not supported on the instruction flow

2.4.2 BRKx_STAT
This 8 bit read-write register gives the status of the hardware breakpoint unit x. Each status bit can be cleared by writing 1 to it. After a POR, this register is set to 0x00.
Register Name	Address	Bit Field
		7	6	5	4	3	2	1	0
BRKx_STAT	0x09, 0x0D, 0x11, 0x15	Reserved		RANGE_WR	RANGE_RD	ADDR1_WR	ADDR1_RD	ADDR0_WR	ADDR0_RD

• RANGE_WR	: This bit is set whenever the CPU performs a write access within the BRKx_ADDR0→BRKx_ADDR1 range (valid if RANGE_MODE=1 and ACCESS_MODE[1]=1).
• RANGE_RD	: This bit is set whenever the CPU performs a read access within the BRKx_ADDR0→BRKx_ADDR1 range (valid if RANGE_MODE=1 and ACCESS_MODE[0]=1). / Note: range mode is not supported by the core unless the `DBG_HWBRK_RANGE define is set to 1'b1 in the openMSP430_define.v file.
• ADDR1_WR	: This bit is set whenever the CPU performs a write access at the BRKx_ADDR1 address (valid if RANGE_MODE=0 and ACCESS_MODE[1]=1).
• ADDR1_RD	: This bit is set whenever the CPU performs a read access at the BRKx_ADDR1 address (valid if RANGE_MODE=0 and ACCESS_MODE[0]=1).
• ADDR0_WR	: This bit is set whenever the CPU performs a write access at the BRKx_ADDR0 address (valid if RANGE_MODE=0 and ACCESS_MODE[1]=1).
• ADDR0_RD	: This bit is set whenever the CPU performs a read access at the BRKx_ADDR0 address (valid if RANGE_MODE=0 and ACCESS_MODE[0]=1).

2.4.3 BRKx_ADDR0
This 16 bit read-write register holds the value which is compared against the address value currently present on the program or data address bus. After a POR, this register is set to 0x0000.
Register Name	Address	Bit Field
		15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
BRKx_ADDR0	0x0A, 0x0E, 0x12, 0x16	BRK_ADDR0[15:0]

• BRK_ADDR0	: Value compared against the address value currently present on the program or data address bus.

2.4.4 BRKx_ADDR1
This 16 bit read-write register holds the value which is compared against the address value currently present on the program or data address bus. After a POR, this register is set to 0x0000.
Register Name	Addresses	Bit Field
		15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
BRKx_ADDR1	0x0B, 0x0F, 0x13, 0x17	BRK_ADDR1[15:0]

• BRK_ADDR1	: Value compared against the address value currently present on the program or data address bus.

3. Debug Communication Interface: UART

With its UART interface, the openMSP430 debug unit can communicate with the host computer using a simple RS232 cable (connected to the dbg_uart_txd and dbg_uart_rxd ports of the IP).
Typically, a USB to RS232 or USB to serial TTL cable will provide a reliable communication link between your host PC and the openMSP430 (speed being typically limited by the cable length).

3.1 Serial communication protocol: 8N1
There are plenty tutorials on Internet regarding RS232 based protocols. However, here is quick recap about 8N1 (1 Start bit, 8 Data bits, No Parity, 1 Stop bit):
As you can see in the above diagram, data transmission starts with a Start bit, followed by the data bits (LSB sent first and MSB sent last), and ends with a "Stop" bit.

3.2 Synchronization frame
After a POR, the Serial Debug Interface expects a synchronization frame from the host computer in order to determine the communication speed (i.e. the baud rate).
The synchronization frame looks as following:
As you can see, the host simply sends the 0x80 value. The openMSP430 will then measure the time between the falling and rising edge, divide it by 8 and automatically deduce the baud rate it should use to properly communicate with the host.
Important note: if you want to change the communication speed between two debugging sessions, the Serial Debug Interface needs to go through a reset cycle (i.e. through the reset_n or dbg_en pins) and a new synchronization frame needs to be send.

3.3 Read/Write access to the debug registers
In order to perform a read / write access to a debug register, the host needs to send a command frame to the openMSP430.
In case of write access, this command frame will be followed by 1 or 2 data frames and in case of read access, the openMSP430 will send 1 or 2 data frames after receiving the command.
3.3.1 Command Frame
The command frame looks as following:

• WR	: Perform a Write access when set. Read otherwise.
• B/W	: Perform a 8-bit data access when set (one data frame). 16-bit otherwise (two data frame).
• Address	: Debug register address.

3.3.2 Write access
A write access transaction looks like this:

3.3.3 Read access
A read access transaction looks like this:

3.4 Read/Write burst implementation for the CPU Memory access
In order to optimize the data burst transactions for the UART, read/write access are not done by reading or writing the MEM_DATA register.
Instead, the data transfer starts immediately after the MEM_CTL.START bit has been set.

3.4.1 Write Burst access
A write burst transaction looks like this:

3.4.2 Read Burst access
A read burst transaction looks like this:

4. Debug Communication Interface: I2C

With its I2C interface, the openMSP430 debug unit can communicate with the host computer using an I2C adapter (connected to the dbg_i2c_scl and dbg_i2c_sda_in/dbg_i2c_sda_out ports of the IP).
Currently, the USB-ISS adapter from Devantech (Robot Electronics) is supported by the software development tools and provides a reliable communication link between your host PC and the openMSP430.

4.1 I2C communication protocol
There are plenty tutorials on Internet regarding the I2C protocol (see the official I2C specification for more info).
A simple byte read or write frame looks as following:

4.2 Synchronization frame
Unlike the UART interface, the I2C is a synchronous communication protocol.
A synchronization frame is therefore not required.

4.3 Read/Write access to the debug registers
In order to perform a read / write access to a debug register, the host needs to send a command frame to the openMSP430.
In case of write access, this command frame will be followed by 1 or 2 data frames and in case of read access, the openMSP430 will send 1 or 2 data frames after receiving the command.

4.3.1 Command Frame
The command frame looks as following:
• WR	: Perform a Write access when set. Read otherwise.
• B/W	: Perform a 8-bit data access when set (one data frame). 16-bit otherwise (two data frame).
• Address	: Debug register address.

4.3.2 Write access
A write access transaction looks like this:
4.3.3 Read access
A read access transaction looks like this:

4.4 Read/Write burst implementation for the CPU Memory access
In order to optimize the data burst transactions for the I2C, read/write access are not done by reading or writing the MEM_DATA register.
Instead, the data transfer starts immediately after the MEM_CTL.START bit has been set.

4.4.1 Write Burst access
A write burst transaction looks like this:

4.4.2 Read Burst access
A read burst transaction looks like this:

.
Integration and Connectivity

Table of content

- 1. Overview
- 2. Clocks
- 3. Resets
- 4. Program Memory
- 5. Data Memory
- 6. Peripherals
- 7. Interrupts
- 8. Serial Debug Interfaces
  - 8.1 UART Configuration
  - 8.2 I2C Configuration

1. Overview

This chapter aims to give a comprehensive description of all openMSP430 core interfaces in order to facilitate its integration within an ASIC or FPGA.
The following diagram shows an overview of the openMSP430 core connectivity in an FPGA system (i.e. all ASIC specific pins are left unused):
The full pinout of the core is summarized in the following table.

Port Name	Direc-tion	Width	Clock Domain	Description
Clocks
cpu_en	Input	1	<async> or mclk4	Enable CPU code execution (asynchronous and non-glitchy). Set to 1 if unused.
dco_clk	Input	1	-	Fast oscillator (fast clock)
lfxt_clk	Input	1	-	Low frequency oscillator (typ. 32KHz) Set to 0 if unused.
mclk	Output	1	-	Main system clock
aclk_en	Output	1	mclk	FPGA ONLY: ACLK enable
smclk_en	Output	1	mclk	FPGA ONLY: SMCLK enable
dco_enable	Output	1	dco_clk	ASIC ONLY: Fast oscillator enable
dco_wkup	Output	1	<async>	ASIC ONLY: Fast oscillator wakeup (asynchronous)
lfxt_enable	Output	1	lfxt_clk	ASIC ONLY: Low frequency oscillator enable
lfxt_wkup	Output	1	<async>	ASIC ONLY: Low frequency oscillator wakeup (asynchronous)
aclk	Output	1	-	ASIC ONLY: ACLK
smclk	Output	1	-	ASIC ONLY: SMCLK
wkup	Input	1	<async>	ASIC ONLY: System Wake-up (asynchronous and non-glitchy) Set to 0 if unused.
Resets
puc_rst	Output	1	mclk	Main system reset
reset_n	Input	1	<async>	Reset Pin (active low, asynchronous and non-glitchy)
Program Memory interface
pmem_addr	Output	`PMEM_ / AWIDTH1	mclk	Program Memory address
pmem_cen	Output	1	mclk	Program Memory chip enable (low active)
pmem_din	Output	16	mclk	Program Memory data input (optional2)
pmem_dout	Input	16	mclk	Program Memory data output
pmem_wen	Output	2	mclk	Program Memory write byte enable (low active) (optional2)
Data Memory interface
dmem_addr	Output	`DMEM_ / AWIDTH1	mclk	Data Memory address
dmem_cen	Output	1	mclk	Data Memory chip enable (low active)
dmem_din	Output	16	mclk	Data Memory data input
dmem_dout	Input	16	mclk	Data Memory data output
dmem_wen	Output	2	mclk	Data Memory write byte enable (low active)
External Peripherals interface
per_addr	Output	14	mclk	Peripheral address
per_din	Output	16	mclk	Peripheral data input
per_dout	Input	16	mclk	Peripheral data output
per_en	Output	1	mclk	Peripheral enable (high active)
per_we	Output	2	mclk	Peripheral write byte enable (high active)
Interrupts
irq	Input	`IRQ_NR-21	mclk	Maskable interrupts (one-hot signal)
nmi	Input	1	<async> or mclk4	Non-maskable interrupt (asynchronous)
irq_acc	Output	`IRQ_NR-21	mclk	Interrupt request accepted (one-hot signal)
Serial Debug interface
dbg_en	Input	1	<async> or mclk4	Debug interface enable (asynchronous)3
dbg_freeze	Output	1	mclk	Freeze peripherals
dbg_uart_txd	Output	1	mclk	Debug interface: UART TXD
dbg_uart_rxd	Input	1	<async>	Debug interface: UART RXD (asynchronous)
dbg_i2c_addr	Input	7	mclk	Debug interface: I2C Address
dbg_i2c_broadcast	Input	7	mclk	Debug interface: I2C Broadcast Address (for multicore only)
dbg_i2c_scl	Input	1	<async>	Debug interface: I2C SCL
dbg_i2c_sda_in	Input	1	<async>	Debug interface: I2C SDA input
dbg_i2c_sda_out	Output	1	mclk	Debug interface: I2C SDA output
Scan
scan_enable	Input	1	dco_clk	ASIC ONLY: Scyn enable (active during scan shifting)
scan_mode	Input	1	<stable>	ASIC ONLY: Scan mode

1: This parameter is declared in the openMSP430_defines.v file and defines the RAM/ROM size or the number of interrupts vectors (16, 32 or 64).
2: These two optional ports can be connected whenever the program memory is a RAM. This will allow the user to load a program through the serial debug interface and to use software breakpoints.
3: When disabled, the debug interface is hold into reset (and clock gated in ASIC mode). As a consequence, the dbg_en port can be used to reset the debug interface without disrupting the CPU execution.
4: Clock domain is selectable through configuration in the openMSP430_defines.v file (see Advanced System Configuration).

2. Clocks
The different clocks in the design are managed by the Basic Clock Module as following in the FPGA configuration:
or as following in the ASIC configuration:
- CPU_EN: this input port provides a hardware mean to stop or resume CPU execution. When unused, this port should be set to 1.
- DCO_CLK: this input port is typically connected to a PLL, RC oscillator or any clock resource the target FPGA/ASIC might provide.
  From a synthesis tool perspective (ISE, Quartus, Libero, Design Compiler...), this the only port where a clock needs to be declared.
- LFXT_CLK: in an FPGA system, if ACLK_EN or SMCLK_EN are going to be used in the project (for example through the Watchdog or TimerA peripherals), then this port needs to be connected to a clock running at least two time slower as DCO_CLK (typically 32kHz). It can be connected to 0 or 1 otherwise.
  In an ASIC, if ACLK or SMCLK are used and if the clock muxes are included, then this port can be connected to any kind of clock source (it doesn't need to be low-frequency. The name was just kept to be consistent with TI's documentation).
- MCLK: the main system clock drives the complete openMSP430 clock domain, including program/data memories and the peripheral interfaces.
- ACLK_EN / SMCLK_EN: these two clock enable signals can be used in order to emulate the original ACLK and SMCLK from the MSP430 specification when the core is targeting an FPGA.
  An example of this can be found in the Watchdog and TimerA modules, where it is implemented as following:
- ACLK / SMCLK: ACLK and MCLK are available through these two ports when targeting an ASIC.
- DCO_ENABLE / DCO_WKUP: ASIC specific signals controlling the fast clock generator for low power mode support (SCG0 bit in the status register).
- LFXT_ENABLE / LFXT_WKUP: ASIC specific signals controlling the low frequency clock generator for low power mode support (OSCOFF bit in the status register).
- WKUP: When activated, this signal allows a peripheral to restore all CPU clocks (i.e. wakeup the cpu) prior IRQ generation. Note that IRQs MUST always be generated from the MCLK clock domain.

As an FPGA system illustration, the following waveform shows the different clocks where the software running on the openMSP430 configures the BCSCTL1 and BCSCTL2 registers so that ACLK_EN and SMCLK_EN are respectively running at LFXT_CLK/2 and DCO_CLK/4.

3. Resets

- RESET_N: this input port is typically connected to a board push button and is generally combined with the system power-on-reset.
- PUC_RST: the Power-Up-Clear signal is asynchronously set with the reset pin (RESET_N), the watchdog reset or the serial debug interface reset. In order to get clean timings, it is synchronously cleared with MCLK. As a general rule, this signal should be used as the reset of the MCLK clock domain.

The following waveform illustrates this:

4. Program Memory

Depending on the project needs, the program memory can be either implemented as a ROM or RAM.

If a ROM is selected then the PMEM_DIN and PMEM_WEN ports won't be connected. In that case, the software debug capabilities are limited because the serial debug interface can only use hardware breakpoints in order to stop the program execution. In addition, updating the software will require a reprogramming of the FPGA... or a new ROM mask for an ASIC.

If the program memory is a RAM, the developer gets full flexibility regarding software debugging. The serial debug interface can be used to update the program memory and software breakpoints can be used.

That said, the protocol between the openMSP430 and the program memory is quite standard. Signal description goes as following:

- PMEM_CEN: when this signal is active, the read/write access will be executed with the next MCLK rising edge. Note that this signal is LOW ACTIVE.
- PMEM_ADDR: Memory address of the 16 bit word which is going to be accessed.
  Note: in order to calculate the core logical address from the program memory physical address, the formula goes as following: LOGICAL@=2*PHYSICAL@+0x10000-PMEM_SIZE
- PMEM_DOUT: the memory output word will be updated with every valid read/write access (i.e. PMEM_DOUT is not updated if PMEM_CEN=1).
- PMEM_WEN: this signal selects which byte should be written during a valid access. PMEM_WEN[0] will activate a write on the lower byte, PMEM_WEN[1] a write on the upper byte. Note that these signals are LOW ACTIVE.
- PMEM_DIN: the memory input word will be written with the valid write access according to the PMEM_WEN value.

The following waveform illustrates some read accesses of the program memory (write access are illustrated in the data memory section):

5. Data Memory

The data memory is always implemented as a RAM.

The protocol between the openMSP430 and the data memory is the same as the one of the program memory. Therefore, the signal description is the same:

- DMEM_CEN: when this signal is active, the read/write access will be executed with the next MCLK rising edge. Note that this signal is LOW ACTIVE.
- DMEM_ADDR: Memory address of the 16 bit word which is going to be accessed.
  Note: in order to calculate the core logical address from the data memory physical address, the formula goes as following: LOGICAL@=2*PHYSICAL@+0x200
- DMEM_DOUT: the memory output word will be updated with every valid read/write access (i.e. DMEM_DOUT is not updated if DMEM_CEN=1).
- DMEM_WEN: this signal selects which byte should be written during a valid access. DMEM_WEN[0] will activate a write on the lower byte, DMEM_WEN[1] a write on the upper byte. Note that these signals are LOW ACTIVE.
- DMEM_DIN: the memory input word will be written with the valid write access according to the DMEM_WEN value.

The following waveform illustrates some read/write access to the data memory:

6. Peripherals

The protocol between the openMSP430 core and its peripherals is the exactly same as the one with the data and program memories in regard to write access and differs slightly for read access.
On the connectivity side, the specificity is that the read data bus of all peripherals should be ORed together before being connected to the core, as showed in the diagram of the Overview section.
From the logical point of view, during a read access, each peripheral outputs the combinatorial value of its read mux and returns 0 if it doesn't contain the addressed register. On the waveforms, this translates by seeing the register value on PER_DOUT while PER_EN is valid and not one clock cycle afterward as it is the case with the program and data memories.
In any case, it is recommended to use the templates provided with the core in order to develop your own custom peripherals.

The signal description therefore goes as following:

- PER_EN: when this signal is active, read access are executed during the current MCLK cycle while write access will be executed with the next MCLK rising edge. Note that this signal is HIGH ACTIVE.
- PER_ADDR: peripheral register address of the 16 bit word which is going to be accessed. It is to be noted that a 14 bit address will always be provided from the openMSP430 to the peripheral in order to accommodate the biggest possible PER_SIZE Verilog configuration option (i.e. 32kB as opposed to 512B by default).
  Note: in order to calculate the core logical address from the peripheral register physical address, the formula goes as following: LOGICAL@=2*PHYSICAL@
- PER_DOUT: the peripheral output word will be updated with every valid read/write access, it will be set to 0 otherwise.
- PER_WE: this signal selects which byte should be written during a valid access. PER_WE[0] will activate a write on the lower byte, PER_WE[1] a write on the upper byte. Note that these signals are HIGH ACTIVE.
- PER_DIN: the peripheral input word will be written with the valid write access according to the PER_WEN value.

The following waveform illustrates some read/write access to the peripheral registers:

7. Interrupts

As with the original MSP430, the interrupt priorities of the openMSP430 are fixed in hardware accordingly to the connectivity of the NMI and IRQ ports.
If two interrupts are pending simultaneously, the higher priority interrupt will be serviced first.
The following table summarize this:
Interrupt Port	Vector address	Priority
RESET_N	0xFFFE	15 (highest)
NMI	0xFFFC	14
IRQ[13]	0xFFFA	13
IRQ[12]	0xFFF8	12
IRQ[11]	0xFFF6	11
IRQ[10]	0xFFF4	10
IRQ[9]	0xFFF2	9
IRQ[8]	0xFFF0	8
IRQ[7]	0xFFEE	7
IRQ[6]	0xFFEC	6
IRQ[5]	0xFFEA	5
IRQ[4]	0xFFE8	4
IRQ[3]	0xFFE6	3
IRQ[2]	0xFFE4	2
IRQ[1]	0xFFE2	1
IRQ[0]	0xFFE0	0 (lowest)

The signal description goes as following:
- NMI: The Non-Maskable Interrupt has higher priority than other IRQs and is masked by the NMIIE bit instead of GIE.
  It is internally synchronized to the MCLK domain and can therefore be connected to any asynchronous signal of the chip (which could for example be a pin of the FPGA). If unused, this signal should be connected to 0.
- IRQ: The standard interrupts can be connected to any signal coming from the MCLK domain (typically a peripheral). Priorities can be chosen by selecting the proper bit of the IRQ bus as shown in the table above. Unused interrupts should be connected to 0.
  Note: IRQ[10] is internally connected to the Watchdog interrupt. If this bit is also used by an external peripheral, they will both share the same interrupt vector.
- IRQ_ACC: Whenever an interrupt request is serviced, some peripheral automatically clear their pending flag in hardware. In order to do so, the IRQ_ACC bus can be used by using the bit matching the corresponding IRQ bit. An example of this is shown in the implementation of the TACCR0 Timer A interrupt.

The following waveform illustrates a TAIV interrupt issued by the Timer-A, which is connected to IRQ[8]:

8. Serial Debug Interface

The serial debug interface module provides a two-wires communication bus for remote debugging and an additional freeze signal which might be useful for some peripherals (typically timers).

- DBG_EN: this signal allows the user to enable or disable the serial debug interface without interfering with the CPU execution. It is to be noted that when disabled (i.e. DBG_EN=0), the debug interface is held into reset.
- DBG_FREEZE: this signal will be set whenever the debug interface stops the CPU (and if the FRZ_BRK_EN field of the CPU_CTL debug register is set). As its name implies, the purpose of DBG_FREEZE is to freeze a peripheral whenever the CPU is stopped by the software debugger.
  For example, it is used by the Watchdog timer in order to stop its free-running counter. This prevents the CPU from being reseted by the watchdog every times the user stops the CPU during a debugging session.

8.1 UART Configuration

DBG_UART_TXD / DBG_UART_RXD: these signals are typically connected to an RS-232 transceiver and will allow a PC to communicate with the openMSP430 core.

The following waveform shows some communication traffic on the serial bus :

8.2 I2C Configuration

- DBG_I2C_ADDR: I2C Device address of the oMSP core (between 8 and 119). In a multi-core configuration, each core has its own address.
- DBG_I2C_BROADCAST: I2C Device broadcast address of the oMSP core (between 8 and 119). In a multi-core configuration, all cores have the same broadcast address.
- DBG_I2C_SCL: I2C bus clock input (SCL).
- DBG_I2C_SDA_OUT / DBG_I2C_SDA_IN: these signals are connected to the SDA I/O cell as following:

The following waveform shows some communication traffic on the I2C bus:

.
ASIC Implementation
Table of content
- 1. Introduction
- 2. RTL Configuration
  - 2.1 Basic Clock Module
    - 2.1.1 Low-frequency clock domain
    - 2.1.2 Clock muxes
    - 2.1.3 Clock dividers
    - 2.1.4 Low-Power modes
      - 2.1.4.1 Internal clocks ( MCLK / SMCLK )
      - 2.1.4.2 Clock oscillators ( DCO_CLK / LFXT_CLK )
  - 2.2 Other configuration options
    - 2.2.1 Fine grained clock gating
    - 2.2.2 Watchdog clock mux
- 3. DFT considerations
  - 3.1 Resets
  - 3.2 Clock Gates
  - 3.3 Clock Muxes
  - 3.4 Coverage
- 4. Sensitive modules
  - 4.1 AND Gate ( omsp_and_gate.v )
  - 4.2 Clock Gate ( omsp_clock_gate.v )
  - 4.3 Clock Mux ( omsp_clock_mux.v )
  - 4.4 Scan Mux ( omsp_scan_mux.v )
  - 4.5 Sync Cell ( omsp_sync_cell.v )
  - 4.6 Sync Reset ( omsp_sync_reset.v )
  - 4.7 Wakeup Cell ( omsp_wakeup_cell.v )

1. Introduction

This section covers specific points of the openMSP430 ASIC implementation, in particular:
    - The ASIC specific RTL configuration options.
    - Some DFT considerations.
    - A description of each ASIC sensitive module.
Keep in mind that as no exotic design technique were used in the openMSP430, following a standard implementation flow from Synthesis to P&R is the best way to go.

2. RTL Configuration

Whenever the "`define ASIC" statement of the Expert System Configuration section is uncommented, all ASIC specific configuration options are enabled.

2.1 Basic Clock Module

In its ASIC configuration, the Basic clock module of the openMSP430 can support up to all features described in the MSP430x1xx Family User's Guide (Chapter 4).
In particular, the ASIC_CLOCKING option activates all advancd clocking options (note that formal equivalence with the FPGA version is achieved by commenting this option out):
//=============================================================== // ASIC CLOCKING //=============================================================== //------------------------------------------------------- // When uncommented, this define will enable the ASIC // architectural clock gating as well as the advanced low // power modes support (most common). // Comment this out in order to get FPGA-like clocking. //------------------------------------------------------- `define ASIC_CLOCKING

All these advanced clocking options are highlighted in the following diagram and discussed below:

2.1.1 Low-Frequency Clock Domain
The LFXT clock domain can be enabled thanks to the following configuration option:
//============================================================================ // LFXT CLOCK DOMAIN //============================================================================ //------------------------------------------------------------- // When uncommented, this define will enable the lfxt_clk // clock domain. // When commented out, the whole chip is clocked with dco_clk. //------------------------------------------------------------- `define LFXT_DOMAIN

Note 1: When commented-out:
    - ACLK is running on DCO_CLK
    - MCLK_MUX and SMCLK_MUX options are not supported
    - OSCOFF_EN low power mode is not supported
Note 2: Unlike its name suggest, there is no frequency limitation on LFXT_CLK. The name was simply kept in order to be consistent with the original MSP430 documentation, where LFXT_CLK is typically connected to a 32 kHz crystal oscillator.
2.1.2 Clock Muxes
The MCLK and SMCLK clock muxes can be enabled or disabled with the following options:
//============================================================================ // CLOCK MUXES //============================================================================ //------------------------------------------------------- // MCLK: Clock Mux //------------------------------------------------------- // When uncommented, this define will enable the // MCLK clock MUX allowing the selection between // DCO_CLK and LFXT_CLK with the BCSCTL2.SELMx register. // When commented, DCO_CLK is selected. //------------------------------------------------------- `define MCLK_MUX //------------------------------------------------------- // SMCLK: Clock Mux //------------------------------------------------------- // When uncommented, this define will enable the // SMCLK clock MUX allowing the selection between // DCO_CLK and LFXT_CLK with the BCSCTL2.SELS register. // When commented, DCO_CLK is selected. //------------------------------------------------------- `define SMCLK_MUX

Note 1: When a MUX is excluded, the concerned clock (MCLK and/or SMCLK) is running with DCO_CLK.
Note 2: If a MUX is included, the implementation and sign-off tools (in particular CTS and STA) must be aware that a new clock needs to be defined on the MUX output.
2.1.3 Clock Dividers
The MCLK, SMCLK and ACLK clock dividers can be enabled or disabled with the following options:
//============================================================================ // CLOCK DIVIDERS //============================================================================ //------------------------------------------------------- // MCLK: Clock divider //------------------------------------------------------- // When uncommented, this define will enable the // MCLK clock divider (/1/2/4/8) //------------------------------------------------------- `define MCLK_DIVIDER //------------------------------------------------------- // SMCLK: Clock divider (/1/2/4/8) //------------------------------------------------------- // When uncommented, this define will enable the // SMCLK clock divider //------------------------------------------------------- `define SMCLK_DIVIDER //------------------------------------------------------- // ACLK: Clock divider (/1/2/4/8) //------------------------------------------------------- // When uncommented, this define will enable the // ACLK clock divider //------------------------------------------------------- `define ACLK_DIVIDER

The clock dividers instantiate a clock gate on the clock tree and are implemented as following:

2.1.4 Low-Power Modes

2.1.4.1 Internal clocks ( MCLK / SMCLK )
Two bit fields in the status register (R2) allow to control the system clocks:
    - CPUOFF allows to switch-off MCLK
    - SCG1 allows to switch-off SMCLK
These control bits are supported by the openMSP430 and can be included in the design with the following defines:
//============================================================================ // LOW POWER MODES //============================================================================ //------------------------------------------------------- // LOW POWER MODE: CPUOFF //------------------------------------------------------- // When uncommented, this define will include the // clock gate allowing to switch off MCLK in // all low power modes: LPM0, LPM1, LPM2, LPM3, LPM4 //------------------------------------------------------- `define CPUOFF_EN //------------------------------------------------------- // LOW POWER MODE: SCG1 //------------------------------------------------------- // When uncommented, this define will include the // clock gate allowing to switch off SMCLK in // the following low power modes: LPM2, LPM3, LPM4 //------------------------------------------------------- `define SCG1_EN

In order to keep the clock tree as flat as possible, the CPUOFF and SCG1 low power options share the same clock gate with the clock divider:

2.1.4.2 Clock oscillators ( DCO_CLK / LFXT_CLK )
There are two bit fields in the status register (R2) allowing to control the clock oscillators:
    - SCG0 allows to switch-off the DCO oscillator
    - OSCOFF allows to switch-off the LFXT oscillator
These control bits are supported by the openMSP430 and can be included in the design with the following defines:
//============================================================================ // LOW POWER MODES //============================================================================ //------------------------------------------------------- // LOW POWER MODE: SCG0 //------------------------------------------------------- // When uncommented, this define will enable the // DCO_ENABLE/WKUP port control (always 1 when commented). // This allows to switch off the DCO oscillator in the // following low power modes: LPM1, LPM3, LPM4 //------------------------------------------------------- `define SCG0_EN //------------------------------------------------------- // LOW POWER MODE: OSCOFF //------------------------------------------------------- // When uncommented, this define will include the // LFXT_CLK clock gate and enable the LFXT_ENABLE/WKUP // port control (always 1 when commented). // This allows to switch off the low frequency oscillator // in the following low power modes: LPM4 //------------------------------------------------------- `define OSCOFF_EN

The control logic of both DCO and LFXT oscillators is identical.
When disabled, the *_WKUP signal is used to asynchronously wake up the oscillator. Once the oscillator is awake (and therefore a clock is available), the *_ENABLE signal will take over and synchronously keep the oscillator enabled until the CPU clears the SCG0 or OSCOFF bit again.
The following two waveforms illustrate the CPU entering the LPM1 mode, and in particular the DCO oscillator being switched-off:
Entering LPM1 through a BIS #N, R2 instruction:

- Entering LPM1 through a RETI instruction:

Note: the DCO oscillator is enabled until the BIS and RETI instruction are fully executed (i.e. until the CPU state machines reach their IDLE state).
At last, this waveform shows the CPU going out of LPM1 mode and in particular the DCO oscillator wake-up sequence:

In order to wake-up the CPU from ANY low power mode, the system MUST ALWAYS go through the following chain of events (as illustrated in the previous waveform):
    - The peripheral (for example a timer) asserts the WKUP input of the openMSP430 in order to asynchronously restore the clocks. At this stage, DCO_WKUP is activated and DCO_ENABLE is still cleared.
    - Once MCLK is available, the peripheral generates a synchronous IRQ signal in order to re-activate the CPU state machines.
    - The CPU state machines activated, DCO_ENABLE is synchronously set.
    - When the global interrupt enable flag (GIE) is cleared, DCO_WKUP is released two clock cycles later (i.e. same behavior as a reset synchronizer).
      Important note: the peripheral should release the WKUP input when its interrupt pending flag is cleared. Otherwise the DCO_WKUP signal will be set again as soon as the GIE flag is restored by the RETI instruction... which is probably not the intended behavior :-P
    - The DCO oscillator is now enabled until SCG0 is set again.

2.2 Other configuration options

2.2.1 Fine Grained Clock Gating
Nowadays, all synthesis tools support automatic (fine grained) clock gating insertion.
However, as some design houses still prefer to have the clock gates directly instantiated in the RTL, there is the possibility to include the 'manual' fine grained clock gates in the design with the following define:
//============================================================================ // FINE GRAINED CLOCK GATING //============================================================================ //------------------------------------------------------- // When uncommented, this define will enable the fine // grained clock gating of all registers in the core. //------------------------------------------------------- `define CLOCK_GATING

2.2.2 Watchdog Clock Mux
The watchdog clock mux allows to select between ACLK and SMCLK. It can be enabled or disabled with the WATCHDOG_MUX define.
When excluded, the additional WATCHDOG_NOMUX_ACLK option allows the user to decide if the watchdog clock should be hard-wired to ACLK (if uncommented) or SMCLK (if commented-out)
//============================================================================ // CLOCK MUXES //============================================================================ //------------------------------------------------------- // WATCHDOG: Clock Mux //------------------------------------------------------- // When uncommented, this define will enable the // Watchdog clock MUX allowing the selection between // ACLK and SMCLK with the WDTCTL.WDTSSEL register. // When commented out, ACLK is selected if the // WATCHDOG_NOMUX_ACLK define is uncommented, SMCLK is // selected otherwise. //------------------------------------------------------- `define WATCHDOG_MUX //`define WATCHDOG_NOMUX_ACLK

3. DFT Considerations

The openMSP430 is designed to be fully scan friendly. During production, the ATE controls the core through the scan_mode and scan_enable signals. The scan_mode port is always asserted during scan testing and is used to switch between functional and scan mode.

3.1 Resets
When in scan mode (i.e. scan_mode input port is set), ALL internal resets of the openMSP430 are connected the reset_n input port.
Taking the POR generation as an example, it is implemented using the omsp_scan_mux module as following:

3.2 Clock Gates
When in scan mode (i.e. scan_mode input port is set), ALL clock gates instantiated in the design must be enabled during scan shifting. This is can be achieved by setting the scan_enable input port during the shift phase.
On the other hand, during the capture phase, the scan_enable port must be cleared in order to restore the functional behavior of the clock gate.
This feature is implemented in the omsp_clock_gate module as following:

3.3 Clock Muxes
When in scan mode (i.e. scan_mode input port is set), the MCLK and SMCLK clock muxes are both running on DCO_CLK. The watchdog mux is running SMCLK (i.e. DCO_CLK).
This feature is implemented in the omsp_clock_mux module as following:

Note: if the LFXT clock domain is enabled, the LFXT_CLK input port should also be connected to the scan clock when in scan mode.

3.4 Coverage
After synthesizing the openMSP430 in its maximum configuration (in particular with ALL clock domains available and ALL clock muxes included), the core reaches 99.7%stuck-at fault coverage:

4. Sensitive Modules

ALL modules discussed in this section have a simple and well defined functionality but nonetheless lay on sensitive parts of the design (clock tree, wake-up path, ...).
In the industry, it is common place for companies to have policies recommending designers to use textbook structures or specific standard cells when implementing circuits considered as 'sensitive'.
This section will hopefully help to quickly identify these 'sensitive' circuits and adapt them to your requirements if necessary.

4.1 AND Gate ( omsp_and_gate.v )

This module implements a simple AND2 gate and is instantiated several times on the wake-up paths in order to ensure a glitch free generation of the wake-up signals. The idea behind this block is to prevent the synthesis tool from optimizing the combinatorial wake-up path and potentially generate a glitchy logic.
There are three different ways to handle this block:
1. Do nothing
2. Modify the RTL by directly instantiating an AND2 cell from the target library and applying a don't touch or size only attribute on it before proceeding to the synthesis compile step
3. Keep the RTL unchanged and when running synthesis, first compile this module separately before going to the top down compile (don't forget the don't touch or size only attribute)

Note that the first option is actually acceptable because in low power mode, there are no clocks available, which means no glitch... However, in active mode, the wake-up line could see a lot of glitches, which is functionally not a problem (since the core is awake anyway) but could be considered as not really elegant...

4.2 Clock Gate ( omsp_clock_gate.v )

Almost every company has a different policy for handling clock gates. Therefore, this module is probably the most likely to be modified.
So here are the facts:
- There are only rising edge flip-flop in the design1
  → as a consequence clock gates can indifferently park the clock high or low without affecting functionality.
- The enable signal of ALL clock gates in the openMSP430 are generated with the rising edge of the clock
  → this leaves the door open for both LATCH and NAND2 based clock gates.
1: beside for the DCO_ENABLE and LFXT_ENABLE signals and the clock MUXes. However, these can be safely ignored
As a consequence, you can feel free to use:

- A LATCH based clock gate. For example:
- Or a NAND2 based clock gate:

4.3 Clock Mux ( omsp_clock_mux.v )

The clock muxes of the openMSP430 are implemented as following:

In order to make this implementation 100% bullet proof, the RTL could be modified by manually instantiating the NAND2 and AND2 cells directly from the target library (with the associated don't touch or size only attributes of course).
However, if you decide to compile this module as it is, the synthesis tool should normally be smart enough and not mess it up (but PLEASE PLEASE PLEASE double check manually the resulting gate netlist).

4.4 Scan Mux ( omsp_scan_mux.v )

As illustrated in the section 3.1, the scan mux cell allows ALL internal resets to be controllable with the reset_n input port in scan mode.
In addition, the scan mux is also used by the omsp_wakeup_cell (see section 4.7 below).

4.5 Sync Cell ( omsp_sync_cell.v )

The following synchronization cell is instantiated on all clock domain crossing data paths:

4.6 Sync Reset ( omsp_sync_reset.v )

Internal resets are generated using the following standard reset synchronizer:

4.7 Wakeup Cell ( omsp_wakeup_cell.v )

The wakeup cell is the most unconventional module of the openMSP430 design as it contains a flip-flop whose clock and reset are both coming from a data path.
In the openMSP430 core, it is instantiated a single time in the watchdog timer but can also be reused in external custom peripherals.
The implementation of the block looks as following:

The basic idea here is simply to set the WKUP_OUT signal with a rising edge on the WKUP_EVENT port, and clear it when WKUP_CLEAR is active (i.e. level sensitive clear).
In order to give a better perspective from a system point of view, the following diagram shows how the wakeup cell has been used in the particular case of the watchdog timer (note that WDTIFG_CLR_REG and WDTQN_EDGE_REG are both output of a flip-flop and therefore glitch-free):

Note: Wake-up signals can of course be generated in a different way as long as they directly come from a flip-flop (or are certified to be non-glitchy).
For example a simple handshake between the WDT_CLK and MCLK clock domains could have been used to clear the WDT_WKUP signal in a fully synchronous manner.
However, it is to be noted that this handshake would introduce some synchronization delay, which might not be negligible if MCLK and WDT_CLK frequencies are orders of magnitude apart (i.e. several MHz for MCLK and 32kHz for WDT_CLK).
As getting the oscillators back to sleep as fast as possible might prove to be extremely important for low-power designs, this asynchronous solution was selected for the omsp_watchdog implementation.
.
Area and Speed Analysis
Table of content
- 1. Overview
  - 1.1 FPGAs
  - 1.2 ASICs
- 2. Detailed results

Warning: the results presented here might vary depending on the tool versions, applied timing constraints and exact configuration of the openMSP430 core.
The FPGA results were obtained using the free tool versions provided by the vendors (i.e ISE 11.1, QuartusII 9.1 & Libero 8.5).
The ASIC synthesis was run with Synopsys Design Compiler 2007.12 (without dc_ultra or any special feature).

1. Overview

1.1 FPGAs

			Utilization
Manu-facturer	Devices	Info	Basic Config. (Core + Watchdog)	Hardware Multiplier	With debug interface (Software breakpoints)	Additional Hardware breakpoint unit
Xilinx	Spartan 3 Spartan 3E Spartan 3A Spartan 3A DSP Virtex 4	4-inputs LUTs	1 620	+ 200	+ 520	+ 80
	Spartan 6 Virtex 5 Virtex 6	6-inputs LUTs	1 240	+ 150	+ 350	+ 70
Altera	Cyclone II Cyclone III Cyclone IV GX Stratix	LEs	1 550	+ 210	+ 480	+ 110
	Arria GX Arria II GX Stratix II Stratix III	ALUTs	1 030	+ 115	+ 380	+ 90
Actel	ProASIC3E ProASIC3L ProASIC3 Fusion IGLOOe	Tiles	3 550	+ 1 060	+ 1 200	+ 220
-	-	Registers	470	+ 75	+ 140	+ 45

Speed (in MHz, min and max values across all speed grades)
Manufacturer	Devices	Basic Configuration (Core + Watchdog + HW Multiplier)	With debug interface
Xilinx	Spartan 3 Spartan 3E Spartan 3A Spartan 3A DSP	30 - 40	25 - 35
	Spartan 6	40 - 65	35 - 60
	Virtex 4	50 - 70	45 - 60
	Virtex 5	75 - 100	65 - 85
	Virtex 6	90 - 115	75 - 100
Altera	Cyclone II	35 - 45	30 - 45
	Cyclone III Cyclone IV GX	40 - 55	35 - 50
	Arria II GX	65 - 85	60 - 80
	Stratix II	55 - 75	50 - 65
	Stratix III	75 - 95	70 - 90
Actel	ProASIC3E ProASIC3L ProASIC3 Fusion IGLOOe	15 - 25	15 - 25

1.2 ASICs

			Area
Process	Target Frequency	Info	Basic Config. (Core + Watchdog)	Hardware Multiplier	With debug interface (Software breakpoints)	Additional Hardware breakpoint unit
180 nm	50 MHz	kGates	8	+ 2.5	+ 2	+ 0.8
	100 MHz	kGates	10	+ 4.4	+ 2	+ 1.2

2. Detailed results

Detailed results can be found in the PDF documentation (see the online download section).
Software Development Tools
Table of content
- 1. Introduction
- 2. openmsp430-loader
- 3. openmsp430-minidebug
- 4. openmsp430-gdbproxy
- 5. MSPGCC Toolchain
  - 5.1 Compiler options
  - 5.2 MCU selection
  - 5.3 Custom linker script

1. Introduction

Building on the serial debug interface capabilities provided by the openMSP430, three utility programs are provided:
- openmsp430-loader: a simple command line boot loader.
- openmsp430-minidebug: a minimalistic debugger with simple GUI.
- openmsp430-gdbproxy: GDB Proxy server to be used together with MSP430-GDB and the Eclipse, DDD, or Insight graphical front-ends.
All these software development tools have been developed in TCL/TK and were successfully tested on both Linux and Windows (XP/Vista/7).
Note: to be able to execute the scripts, TCL/TK needs to be installed on your system.

In order to connect the host PC to the openMSP430 serial debug interface, a UART or I2C serial cable/adapter is required.

Typically, the following solutions will suit any kind of development board:

UART	I2C
USB to RS232 converter: / USB to Serial TTL converter:	Devantech USB-ISS adapter:

2. openmsp430-loader

This simple program allows the user to load the openMSP430 program memory with an executable file (ELF or Intel-HEX format) provided as argument.
It is typically used in conjunction with 'make' in order to automatically load the program after the compile step (see 'Makefile' from software examples provided with the project's FPGA implementation).
The program can be called with the following syntax:
USAGE : openmsp430-loader.tcl [-device <communication port>] / [-adaptor <adaptor type>] / [-speed <communication speed>] / [-i2c_addr <cpu address>] <elf/ihex-file> / DEFAULT : <communication port> = /dev/ttyUSB0 / <adaptor type> = uart_generic / <communication speed> = 115200 (for UART) / I2C_S_100KHZ (for I2C) / <core address> = 42 / EXAMPLES: openmsp430-loader.tcl -device /dev/ttyUSB0 -adaptor uart_generic -speed 9600 leds.elf / openmsp430-loader.tcl -device COM2: -adaptor i2c_usb-iss -speed I2C_S_100KHZ / -i2c_addr 75 ta_uart.ihex

These screenshots show the script in action under Linux and Windows:

3. openmsp430-minidebug

This small program provides a minimalistic graphical interface enabling simple interaction with the openMSP430:

As you can see from the screenshot, it allows the following actions:
- (1)  Connect to the openMSP430 Serial Debug Interface
- (2)  Load the program memory with an ELF or Intel-HEX file
- (3)  Control the CPU: Reset, Stop, Start and Single-Step and Software breakpoints
- (4)  Read/Write access of the CPU registers
- (5)  Read/Write access of the whole memory range (program, data, peripherals)
- (6)  Basic disassembled view of the loaded program (current PC location is highlighted in green, software breakpoints in yellow, pink and violet)
- (7)  Choose the disassembled view type
- (8)  Source a custom external TCL script.
4. openmsp430-gdbproxy

The purpose of this program is to replace the 'msp430-gdbproxy' utility provided by the mspgcc toolchain.
Typically, a GDB proxy creates a local port for GDB to connect to, and handles the communication with the target hardware. In our case, it is basically a bridge between the RSP communication protocol from GDB and the serial debug interface from the openMSP430.
Schematically the communication flow looks as following:
Like the original 'msp430-gdbproxy' program, 'openmsp430-gdbproxy' can be controlled from the command line. However, it also provides a simple graphical interface:

These two additional screenshots show the script in action together with the Eclipse and DDD graphical frontends:

Tip 1: There are several tutorials on Internet explaining how to configure Eclipse for the MSP430. As an Eclipse newbie, I found the followings quite helpful (the msp430-gdbproxy sections should of course be ignored as we are using our own openmsp430-gdbproxy program :-) ):
- A Step By Step Guide To MSP430 Programming Under Linux (English)
- MSP430 eclipse helios mspgcc4 (German)

Tip 2: You probably want to install this excellent Eclipse plugin (see screenshot above):
- EmbSysRegView

5. MSPGCC Toolchain

5.1 Compiler options

The msp430-gcc compiler accepts the following MSP430 specific command line parameters (copied from the MSPGCC manual page):

-mmcu=	Specify the MCU name
-mno-volatile-workaround	Do not perform a volatile workaround for bitwise operations.
-mno-stack-init	Do not initialize the stack as main()starts.
-minit-stack=	Specify the initial stack address.
-mendup-at=	Jump to the specified routine at the end of main().
-mforce-hwmul	Force use of a hardware multiplier.
-mdisable-hwmul	Do not use the hardware multiplier.
-minline-hwmul	Issue inline code for 32-bit integer operations for devices with a hardware multiplier.
-mnoint-hwmul	Do not disable and enable interrupts around hardware multiplier operations. This makes multiplication faster when you are certain no hardware multiplier operations will occur at deeper interrupt levels.
-mcall-shifts	Use subroutine calls for shift operations. This may save some space for shift intensive applications.

5.2 MCU selection

The following table aims to help selecting the proper MCU name for the -mmcu option during the msp430-gcc call:
-mmcu option	Program / Memory	Data / Memory	Hardware Multiplier
Program Memory Size: 1 kB
msp430x110	1 kB	128 B	No
msp430x1101	1 kB	128 B	No
msp430x2001	1 kB	128 B	No
msp430x2002	1 kB	128 B	No
msp430x2003	1 kB	128 B	No
msp430x2101	1 kB	128 B	No
Program Memory Size: 2 kB
msp430x1111	2 kB	128 B	No
msp430x2011	2 kB	128 B	No
msp430x2012	2 kB	128 B	No
msp430x2013	2 kB	128 B	No
msp430x2111	2 kB	128 B	No
msp430x2112	2 kB	128 B	No
msp430x311	2 kB	128 B	No
Program Memory Size: 4 kB
msp430x112	4 kB	256 B	No
msp430x1121	4 kB	256 B	No
msp430x1122	4 kB	256 B	No
msp430x122	4 kB	256 B	No
msp430x1222	4 kB	256 B	No
msp430x2122	4 kB	256 B	No
msp430x2121	4 kB	256 B	No
msp430x312	4 kB	256 B	No
msp430x412	4 kB	256 B	No
Program Memory Size: 8 kB
msp430x123	8 kB	256 B	No
msp430x133	8 kB	256 B	No
msp430x313	8 kB	256 B	No
msp430x323	8 kB	256 B	No
msp430x413	8 kB	256 B	No
msp430x423	8 kB	256 B	Yes
msp430xE423	8 kB	256 B	Yes
msp430xE4232	8 kB	256 B	Yes
msp430xW423	8 kB	256 B	No
msp430x1132	8 kB	256 B	No
msp430x1232	8 kB	256 B	No
msp430x1331	8 kB	256 B	No
msp430x2131	8 kB	256 B	No
msp430x2132	8 kB	256 B	No
msp430x2232	8 kB	512 B	No
msp430x2234	8 kB	512 B	No
msp430x233	8 kB	1024 B	Yes
msp430x2330	8 kB	1024 B	Yes
Program Memory Size: 12 kB
msp430xE4242	12 kB	512 B	Yes
msp430x314	12 kB	512 B	No
Program Memory Size: 16 kB
msp430x4250	16 kB	256 B	No
msp430xG4250	16 kB	256 B	No
msp430x135	16 kB	512 B	No
msp430x1351	16 kB	512 B	No
msp430x155	16 kB	512 B	No
msp430x2252	16 kB	512 B	No
msp430x2254	16 kB	512 B	No
msp430x315	16 kB	512 B	No
msp430x325	16 kB	512 B	No
msp430x415	16 kB	512 B	No
msp430x425	16 kB	512 B	Yes
msp430xE425	16 kB	512 B	Yes
msp430xW425	16 kB	512 B	No
msp430xE4252	16 kB	512 B	Yes
msp430x435	16 kB	512 B	No
msp430x4351	16 kB	512 B	No
msp430x235	16 kB	2048 B	Yes
msp430x2350	16 kB	2048 B	Yes
Program Memory Size: 24 kB
msp430x4260	24 kB	256 B	No
msp430xG4260	24 kB	256 B	No
msp430x156	24 kB	512 B	No
msp430x4361	24 kB	1024 B	No
msp430x436	24 kB	1024 B	No
msp430x336	24 kB	1024 B	Yes
Program Memory Size: 32 kB
msp430x4270	32 kB	256 B	No
msp430xG4270	32 kB	256 B	No
msp430x147	32 kB	1024 B	Yes
msp430x1471	32 kB	1024 B	Yes
msp430x157	32 kB	1024 B	No
msp430x167	32 kB	1024 B	Yes
msp430x2272	32 kB	1024 B	No
msp430x2274	32 kB	1024 B	No
msp430x337	32 kB	1024 B	Yes
msp430x417	32 kB	1024 B	No
msp430x427	32 kB	1024 B	Yes
msp430xE427	32 kB	1024 B	Yes
msp430xE4272	32 kB	1024 B	Yes
msp430xW427	32 kB	1024 B	No
msp430x437	32 kB	1024 B	No
msp430xG437	32 kB	1024 B	No
msp430x4371	32 kB	1024 B	No
msp430x447	32 kB	1024 B	Yes
msp430x2370	32 kB	2048 B	Yes
msp430x247	32 kB	4096 B	Yes
msp430x2471	32 kB	4096 B	Yes
msp430x1610	32 kB	5120 B	Yes
Program Memory Size: 41 kB
msp430x5438	41 kB	16384 B	No
msp430x5437	41 kB	16384 B	No
msp430x5436	41 kB	16384 B	No
msp430x5435	41 kB	16384 B	No
msp430x5419	41 kB	16384 B	No
msp430x54	41 kB	16384 B	No
Program Memory Size: 48 kB
msp430x1611	48 kB	10240 B	Yes
msp430x248	48 kB	4096 B	Yes
msp430x2481	48 kB	4096 B	Yes
msp430x4783	48 kB	2048 B	Yes
msp430xG438	48 kB	2048 B	No
msp430x4784	48 kB	2048 B
msp430x148	48 kB	2048 B	Yes
msp430x168	48 kB	2048 B	Yes
msp430x1481	48 kB	2048 B	Yes
msp430x448	48 kB	2048 B	Yes
Program Memory Size: 51 kB
msp430xG4617	51 kB	8192 B	Yes
msp430x2418	51 kB	8192 B	Yes
msp430x2618	51 kB	8192 B	Yes
msp430x2417	51 kB	8192 B	Yes
msp430xG4618	51 kB	8192 B	Yes
msp430x2617	51 kB	8192 B	Yes
Program Memory Size: 54 kB
msp430x1612	54 kB	5120 B	Yes
Program Memory Size: 55 kB
msp430x2619	55 kB	4096 B	Yes
msp430xG4619	55 kB	4096 B	Yes
msp430xG4616	55 kB	4096 B	Yes
msp430x2416	55 kB	4096 B	Yes
msp430x2419	55 kB	4096 B	Yes
msp430x2616	55 kB	4096 B	Yes
msp430x2410	55 kB	4096 B	Yes
Program Memory Size: 59 kB
msp430x4794	59 kB	2560 B	Yes
msp430x4793	59 kB	2560 B	Yes
msp430x2491	59 kB	2048 B	Yes
msp430x1491	60 kB	2048 B	Yes
msp430x149	60 kB	2048 B	Yes
msp430xG439	59 kB	2048 B	No
msp430x249	59 kB	2048 B	Yes
msp430x449	59 kB	2048 B	Yes
msp430x169	59 kB	2048 B	Yes

Note: the program memory size should imperatively match the openMSP430 configuration.
5.3 Custom linker script

The use of the -mmcu switch is of course NOT mandatory. It is simply a convenient way to use the pre-existing linker scripts provided with the MSPGCC4 toolchain.
However, if the peripheral address space is larger than the standard 512B of the original MSP430 (see the Advanced System Configuration section), a customized linker script MUST be provided.
To create a custom linker script, the simplest way is to start from an existing one:
- The MSPGCC(4) toolchain provides a wide range of examples for all supported MSP430 models (see “msp430/lib/ldscripts/” sub-directory in the MSPGCC(4) installation directory).
- The openMSP430 project also provide a simple linker script example: ldscript_example.x

From there, the script can be modified to match YOUR openMSP430 configuration:

- In the text (rx) section definition, update the ORIGIN and LENGTH fields to match the PROGRAM MEMORY configuration.
- In the data (rwx) section definition, update the ORIGIN field to match the PERIPHERAL SPACE configuration and the LENGTH field to match the DATA MEMORY configuration.
File and Directory Description
Table of content
- 1. Introduction
- 2. Directory structure: openMSP430 core
- 3. Directory structure: FGPA projects
  - 3.1 Xilinx Spartan 3 example
  - 3.2 Altera Cyclone II example
  - 3.3 Actel ProASIC3 example
- 4. Directory structure: Software Development Tools

1. Introduction

To simplify the integration of this IP, the directory structure is based on the OpenCores recommendations.

2. Directory structure: openMSP430 core
core					openMSP430 Core top level directory
abcd	bench				Top level testbench directory
	abcd	verilog
		abcd	tb_openMSP430.v		Testbench top level module
			ram.v		RAM verilog model
			registers.v		Connections to Core internals for easy debugging
			dbg_uart_tasks.v		UART tasks for the serial debug interface
			dbg_i2c_tasks.v		I2C tasks for the serial debug interface
			io_cell.v		Generic I/O cell model for building the serial debug interface I2C bus
			msp_debug.v		Testbench instruction decoder and ASCII chain generator for easy debugging
			timescale.v		Global time scale definition for simulation.
	doc				Diverse documentation
	abc	slau049f.pdf			MSP430x1xx Family User's Guide
	rtl				RTL sources
	abcd	verilog
		abcd	openMSP430_defines.v		openMSP430 core configuration file (Program and Data memory size definition, Debug Interface configuration)
			openMSP430_undefines.v		openMSP430 Verilog `undef file
			openMSP430.v		openMSP430 top level
			omsp_frontend.v		Instruction fetch and decode
			omsp_execution_unit.v		Execution unit
			omsp_alu.v		ALU
			omsp_register_file.v		Register file
			omsp_mem_backbone.v		Memory backbone
			omsp_clock_module.v		Basic Clock Module
			omsp_sfr.v		Special function registers
			omsp_watchdog.v		Watchdog Timer
			omsp_multiplier.v		16x16 Hardware Multiplier
			omsp_dbg.v		Serial Debug Interface main block
			omsp_dbg_hwbrk.v		Serial Debug Interface hardware breakpoint unit
			omsp_dbg_uart.v		Serial Debug Interface UART communication block
			omsp_dbg_i2c.v		Serial Debug Interface I2C communication block
			omsp_sync_cell.v		Simple synchronization module (double flip-flop).
			omsp_sync_reset.v		Generic Reset synchronizer (double flip-flop).
			omsp_clock_gate.v		Generic Clock gate (NAND2 or LATCH-AND based).
			omsp_clock_mux.v		Standard Clock Mux (used in the clock module & watchdog timer).
			omsp_and_gate.v		AND gate module used on sensitive glitch free data paths.
			omsp_wakeup_cell.v		Generic Wake-up module.
			omsp_scan_mux.v		Scan MUX.
			periph		Peripherals directory
			abcd	omsp_gpio.v	Digital I/O (Port 1 to 6)
				omsp_timerA_defines.v	Timer A configuration file
				omsp_timerA_undefines.v	Timer A Verilog 'undef file
				omsp_timerA.v	Timer A
				template_periph_16b.v	Verilog template for 16 bit peripherals
				template_periph_8b.v	Verilog template for 8 bit peripherals
	sim				Top level simulations directory
	abcd	rtl_sim			RTL simulations
		abcd	bin		RTL simulation scripts
			abcd	msp430sim	Main simulation script for assembler vector sources (located in the src directory)
				msp430sim_c	Main simulation script for C vector sources (located in the src-c directory).
				asm2ihex.sh	Assembly file compilation (Intel HEX file generation)
				ihex2mem.tcl	Verilog program memory file generation
				rtlsim.sh	Verilog Icarus simulation script
				template.x	ASM linker definition file template
				template_defs.asm	Common ASM definition file included in all “.s43” files
				omsp_config.sh	oMSP configuration file.
				parse_results	Script parsing regression log files and generating summary report.
				cov_*	Code coverage scripts for NC-Verilog and ICM
			run		For running RTL simulations
			abcd	run	Run single simulation of a given assembler vector
				run_c	Run single simulation of a given C vector
				run_all	Run regression of all vectors
				run_all_mpy	Run regression of all hardware multiplier vectors (!!! very long simulation time !!!)
				run_disassemble	Disassemble the program memory content of the latest simulation
				run_coverage_analysis	Performs the coverage report merging of the regression run and starts ICM for the analysis.
				load_waveform.sav	SAV file for gtkWave
			src		RTL simulation vectors sources (ASM based)
			abcd	ldscript_example.x	MSPGCC toolchain linker script example
				submit.prj	ISIM simulator verilog command file
				submit.f	Verilog simulator command file
				core.f	Command file listing the CPU files only.
				sing-op_*.s43	Single-operand assembler vector files
				sing-op_*.v	Single-operand verilog stimulus vector files
				two-op_*.s43	Two-operand assembler vector files
				two-op_*.v	Two-operand verilog stimulus vector files
				c-jump_*.s43	Jump assembler vector files
				c-jump_*.v	Jump verilog stimulus vector files
				nmi.s43	NMI assembler vector files
				nmi.v	NMI verilog stimulus vector files
				cpu_startup_asic.s43	CPU startup assembler vector files
				cpu_startup_asic.v	CPU startup stimulus vector files
				op_modes*.s43	CPU operating modes assembler vector files (CPUOFF, OSCOFF, SCG1)
				op_modes*.v	CPU operating modes verilog stimulus vector files (CPUOFF, OSCOFF, SCG1)
				clock_module*.s43	Basic Clock Module assembler vector files
				clock_module*.v	Basic Clock Module verilog stimulus vector files
				lp_modes_*.s43	Low Power modes assembler vector files
				lp_modes_*.v	Low Power modes verilog stimulus vector files
				dbg_*.s43	Serial Debug Interface assembler vector files
				dbg_*.v	Serial Debug Interface verilog stimulus vector files
				sfr.s43	SFR assembler vector files
				sfr.v	SFR verilog stimulus vector files
				gpio_*.s43	Digital I/O assembler vector files
				gpio_*.v	Digital I/O verilog stimulus vector files
				template_periph_*.s43	Peripheral templates assembler vector files
				template_periph_*.v	Peripheral templates verilog stimulus vector files
				wdt_*.s43	Watchdog timer assembler vector files
				wdt_*.v	Watchdog timer verilog stimulus vector files
				tA_*.s43	Timer A assembler vector files
				tA_*.v	Timer A verilog stimulus vector files
				mpy_*.s43	16x16 Multiplier assembler vector files
				mpy_*.v	16x16 Multiplier verilog stimulus vector files
				scan.s43	Scan test assembler vector files
				scan.v	Scan test verilog stimulus vector files
			src-c		RTL simulation vectors sources (C based)
				coremask_v1.0	CoreMark benchmark
				dhrystone_v2.1	Dhrystone benchmark (“official” version)
				dhrystone_4mcu	Dhrystone benchmark (MCU adapted)
				sandbox	Small playground :-)
	synthesis				Top level synthesis directory
	abcd	synopsys			Synopsys (Design Compiler) directory
		abcd	run_syn		Run synthesis
			run_tmax		Run ATPG
			synthesis.tcl		Main synthesis TCL script
			library.tcl		Load library, set operating conditions and wire load models
			read.tcl		Read RTL
			constraints.tcl		Set design constrains
			tmax.tcl		Main TetraMax (ATPG) script
			results		Results directory
		actel			Actel synthesis setup for area & speed analysis
		altera			Altera synthesis setup for area & speed analysis
		xilinx			Xilinx synthesis setup for area & speed analysis

3. Directory structure: FGPA projects
3.1 Xilinx Spartan 3 example
fpga					openMSP430 FPGA Projects top level directory
abcd	xilinx_diligent_s3board					Xilinx FPGA Project based on the Diligent Spartan-3 board
	abcd	bench				Top level testbench directory
		abcd	verilog
			abcd	tb_openMSP430_fpga.v		FPGA testbench top level module
				registers.v		Connections to Core internals for easy debugging
				msp_debug.v		Testbench instruction decoder and ASCII chain generator for easy debugging
				glbl.v		Xilinx "glbl.v" file
				timescale.v		Global time scale definition for simulation.
		doc				Diverse documentation
		abcd	board_user_guide.pdf			Spartan-3 FPGA Starter Kit Board User Guide
			msp430f1121a.pdf			msp430f1121a Specification
			xapp462.pdf			Xilinx Digital Clock Managers (DCMs) user guide
		rtl				RTL sources
		abcd	verilog
			abcd	openMSP430_fpga.v		FPGA top level file
				driver_7segment.v		Four-Digit, Seven-Segment LED Display driver
				io_mux.v		I/O mux for port function selection.
				openmsp430		Local copy of the openMSP430 core. The *define.v file has been adjusted to the requirements of the project.
				coregen		Xilinx's coregen directory
				abcd	ram_8x512_hi.*	512 Byte RAM (upper byte)
				ram_8x512_lo.*	512 Byte RAM (lower byte)
				ram_8x2k_hi.*	2 kByte RAM (upper byte)
				ram_8x2k_lo.*	2 kByte RAM (lower byte)
		sim				Top level simulations directory
		abcd	rtl_sim			RTL simulations
			abcd	bin		RTL simulation scripts
				abcd	msp430sim	Main simulation script
				ihex2mem.tcl	Verilog program memory file generation
				rtlsim.sh	Verilog Icarus simulation script
				run		For running RTL simulations
				abcd	run	Run simulation of a given software project
				run_disassemble	Disassemble the program memory content of the latest simulation
				src		RTL simulation verilog stimulus
				abcd	submit.f	Verilog simulator command file
				*.v	Stimulus vector for the corresponding software project
		software				Software C programs to be loaded in program memory
		abcd	leds			LEDs blinking application (from the CDK4MSP project)
			abcd	makefile
				hardware.h
				main.c
				7seg.h
				7seg.c
			ta_uart			Software UART with Timer_A (from the CDK4MSP project)
		synthesis				Top level synthesis directory
		abcd	xilinx
			abcd	0_create_bitstream.sh		Run Xilinx ISE synthesis in a Linux environment
				1_initialize_pmem.sh		Update bitstream's program memory with a given software ELF file
				2_generate_prom_file.sh		Generate PROM file
				3_program_fpga.sh		Program FPGA and on-board flash memory
				bitstreams
				*.bit	Bitstream files
				*.mcs	PROM files
				README.jpg	README file
				scripts
				ihex2mem.tcl	TCL script converting Intel-HEX format to Verilog memory file.
				impact_generate_prom_file.batch	iMPACT TCL script for PROM file generation.
				impact_program_fpga.batch	iMPACT TCL script for programing FPGA and on-board flash memory.
				memory.bmm	FPGA memory description for bitstream's program memory update
				openMSP430_fpga.ucf	UCF file
				openMSP430_fpga.prj	RTL file list to be synthesized
				xst_verilog.opt	Verilog Option File for XST. Among other things, the search path to the include files is specified here.

3.2 Altera Cyclone II example
fpga					openMSP430 FPGA Projects top level directory
abcd	altera_de1_board					Altera FPGA Project based on Cyclone II Starter Development Board
	abcd	README					README file
		bench					Top level testbench directory
		abcd		verilog
				abcd		tb_openMSP430_fpga.v		FPGA testbench top level module
				registers.v		Connections to Core internals for easy debugging
				msp_debug.v		Testbench instruction decoder and ASCII chain generator for easy debugging
				altsyncram.v		Altera verilog model of the altsyncram module..
				timescale.v		Global time scale definition for simulation.
		doc					Diverse documentation
		abcd	DE1_Board_Schematic.pdf					Cyclone II FPGA Starter Development Board Schematics
			DE1_Reference_Manual.pdf					Cyclone II FPGA Starter Development Board Reference Manual
			DE1_User_Guide.pdf					Cyclone II FPGA Starter Development Board User Guide
		rtl					RTL sources
		abcd	verilog
			abcd		OpenMSP430_fpga.v			FPGA top level file
				driver_7segment.v			Four-Digit, Seven-Segment LED Display driver
				io_mux.v			I/O mux for port function selection.
				ext_de1_sram.v			Interface with altera DE1's external async SRAM (256kwords x 16bits)
				ram16x512.v			Single port RAM generated with the megafunction wizard
				rom16x2048.v			Single port ROM generated with the megafunction wizard
				openmsp430			Local copy of the openMSP430 core. The *define.v file has been adjusted to the requirements of the project.
		sim					Top level simulations directory
		abcd	rtl_sim					RTL simulations
			abcd		bin			RTL simulation scripts
				abcd		msp430sim	Main simulation script
				ihex2mem.tcl	Verilog program memory file generation
				rtlsim.sh	Verilog Icarus simulation script
				run			For running RTL simulations
				abcd		run	Run simulation of a given software project
				run_disassemble	Disassemble the program memory content of the latest simulation
				src			RTL simulation verilog stimulus
				abcd		submit.f	Verilog simulator command file
				*.v	Stimulus vector for the corresponding software project
		software					Software C programs to be loaded in the program memory
		abcd	bin					Specific binaries required for software development.
			abcd		mifwrite.cpp			This prog is taken from http://www.johnloomis.org/ece595c/notes/isa/mifwrite.html and slightly changed to satisfy quartus6.1 *.mif eating engine.
				mifwrite.exe			Windows executable.
				mifwrite			Linux executable.
			memledtest					LEDs blinking application (from the CDK4MSP project)
		synthesis					Top level synthesis directory
		abcd	altera
			abcd		main.qsf			Global Assignments file
				main.sof			SOF file
				OpenMSP430_fpga.qpf			Quartus II project file
				openMSP430_fpga_top.v			RTL file list to be synthesized

3.3 Actel ProASIC3 example
fpga					openMSP430 FPGA Projects top level directory
abcd	actel_m1a3pl_dev_kit					Actel FPGA Project based on the ProASIC3 M1A3PL development kit
	abcd	bench				Top level testbench directory
		abcd	verilog
			abcd	tb_openMSP430_fpga.v		FPGA testbench top level module
				registers.v		Connections to Core internals for easy debugging
				msp_debug.v		Testbench instruction decoder and ASCII chain generator for easy debugging
				dbg_uart_tasks.v		UART tasks for the serial debug interface.
				timescale.v		Global time scale definition for simulation.
				proasic3l.v		Actel ProASIC3L library file.
				DAC121S101.v		Verilog model of National's DAC121S101 12 bit DAC
		doc				Diverse documentation
		abcd	M1A3PL_DEV_KIT_QS.pdf			Development Kit Quickstart Card
			M1IGLOO_StarterKit_v1_5_UG.pdf			Development Kit User's Guide
		rtl				RTL sources
		abcd	verilog
			abcd	openMSP430_fpga.v		FPGA top level file
				dac_spi_if.v		SPI interface to National's DAC121S101 12 bit DAC
				openmsp430		Local copy of the openMSP430 core. The *define.v file has been adjusted to the requirements of the project.
				smartgen		Xilinx's coregen directory
				abcd	dmem_128B.v	128 Byte RAM (for data memory)
				pmem_2kB.v	2 kByte RAM (for program memory)
		sim				Top level simulations directory
		abcd	rtl_sim			RTL simulations
			abcd	bin		RTL simulation scripts
				abcd	msp430sim	Main simulation script
				ihex2mem.tcl	Verilog program memory file generation
				rtlsim.sh	Verilog Icarus simulation script
				run		For running RTL simulations
				abcd	run	Run simulation of a given software project
				run_disassemble	Disassemble the program memory content of the latest simulation
				src		RTL simulation verilog stimulus
				abcd	submit.f	Verilog simulator command file
				*.v	Stimulus vector for the corresponding software project
		software				Software C programs to be loaded in program memory
		abcd	spacewar			SpaceWar oscilloscope game.
			abcd
		synthesis				Top level synthesis directory
		abcd	actel
			abcd	prepare_implementation.tcl		Generate required files prior synthesis and P&R.
				synplify.tcl		Synplify template for the synthesis run.
				libero_designer.tcl		Libero Designer template for the P&R run.
				design_files.v		RTL file list to be synthesized
				design_constraints.pre.sdc		Synthesis timing constraints.
				design_constraints.post.sdc		P&R timing constraints.
				design_constraints.pdc		P&R physical constraints.

4. Directory structure: Software Development Tools

tools				openMSP430 Software Development Tools top level directory
abcd	omsp_alias.xml			This XML file allows the software development tools to identify a openMSP430 implementation, and add customized extra information (Alias, URL, ...).
	bin			Contains the main TCL scripts (and the windows executable files if generated)
	abcd	openmsp430-loader.tcl		Simple command line boot loader
		openmsp430-minidebug.tcl		Minimalistic debugger with simple GUI
		openmsp430-gdbproxy.tcl		GDB Proxy server to be used together with MSP430-GDB and the Eclipse, DDD, or Insight graphical front-ends
		README.TXT		README file regarding the use of TCL scripts in a Windows environment.
	lib			Common library
	abcd	tcl-lib		Common TCL library
		abcd	dbg_uart_generic.tcl	Low level Generic UART communication functions
			dbg_i2c_usb-iss.tcl	Low level I2C communication functions for the USB-ISS adapter
			dbg_utils.tcl	Low level “COMx:” “/dev/tty” communication functions
			dbg_functions.tcl	Main utility functions for the openMSP430 serial debug interface
			combobox.tcl	A combobox listbox widget written in pure tcl (from Bryan Oakley)
			xml.tcl	Simple XML parser (from Keith Vetter).
	openmsp430-gdbproxy			GDB Proxy server main project directory
	abcd	openmsp430-gdbproxy.tcl		GDB Proxy server main TCL Script (symbolic link with the script in the bin directory)
		server.tcl		TCP/IP Server utility functions. Send/Receive RSP packets from GDB.
		commands.tcl		RSP command execution functions.
		doc		Some documentation regarding GDB and the RSP protocol.
		abcd	ew_GDB_RSP.pdf	Document from Bill Gatliff: Embedding with GNU: the gdb Remote Serial Protocol
			Howto-GDB_Remote_Serial_Protocol.pdf	Document from Jeremy Bennett (Embecosm): Howto: GDB Remote Serial Protocol - Writing a RSP Server